## Slide 1: Constructing Minimal Spanning Steiner Trees with Bounded Path Length
Presenter : Cheng-Yin Wu, NTUGIEE
Some of the Slides in this Presentation are Referenced from : Physical Design for Nanometer IC by Prof. Yao-Wen Chang

## Slide 2: Introduction to “Bounded” Tree (1/2)
A real world critical problem
  (Clock Tree) Routing in VLSI Circuit
Source : Physical Design for Nanometer IC by Prof. Yao-Wen Chang

## Slide 3: Introduction to “Bounded” Tree (2/2)
Critical Path Delay (Speed)
  Maximum delay from source to any sink
  Optimum : A shortest path tree rooted at source
Routing Capacitance (Power)
  Power dissipation is linear to routing capacitance
  Optimum : A minimum spanning tree
Draw a balance between : Speed and Power
  Balance between MST and SPT ?!

## Slide 4: MST v.s. SPT Trade-off – Example
Cost (MST) ≤ R + π
Cost (SPT) = (N – 1)R
Source (s)
Sinks
Define R = max distG (s, v ϵ V)
Define Cost(T) = ∑ w(e ϵ T(E))

## Slide 5: Bounded Radius Spanning Tree
Known as Bounded path length minimum spanning tree
radiusT (u) = max distT (u, v ϵ V)
  R = radiusT (s) if T = SPT(s)
Problem Formulation
  Given routing graph G(V, E) with w(e ϵ E) > 0, find a minimal cost routing tree T with
  radiusT (s) ≤ (1 + ε) R for any given ε ≥ 0
  Two extreme cases : MST(ε  ∞) and SPT(ε = 0)
NP-Complete

## Slide 6: Overview of My Following Presentation
Both heuristics and exact algorithms
Heuristics (Sound Not Complete)
  Previous works : BPRIM, BRBC
  This work : BKRUS, BH2
Exact Algorithms (Sound and Complete)
  (Improved) Previous works : BMST_G
  This work : BKEX
To the best of my knowledge, it is the most premier work in tackling this problem
BRBC
BKRUS
BH2
BKEX

## Slide 7: Bounded Radius Bounded Cost Spanning Tree (1/2)
Awerbuch, et al., “Cost-sensitive analysis of communication protocols,” ACM
Symp. Principles of Distributed Computing, 1990.
Cong, Kahng, Robins, Sarrafzadeh, Wong, “Performance-driven global routing
for cell based IC's,” ICCD-91 (and TCAD, June 1992)
One of the first work on this problem
Claims
  radiusT (s) ≤ (1 + ε) R
  Cost(T) ≤ (1 + 2/ε) Cost(MST) (Omit Today)
  Polynomial time Heuristic

## Slide 8: Bounded Radius Bounded Cost Spanning Tree (2/2)
Source : Physical Design for Nanometer IC by Prof. Yao-Wen Chang

## Slide 9: BKRUS : Bounded Kruskal MST
A heuristic similar to BPRIM (previous work), BKRUS extends existing Kruskal MST algorithm to bounded radius cases
  Achieving better performance over benchmarks
Goal : radiusBKT (s) ≤ (1 + ε) R
Classical Kruskal MST Algorithm – Review
  http://www.cs.man.ac.uk/~graham/cs2022/greedy/

## Slide 10: BKRUS Algorithm (1/3)
Extension for upper bound constraint
  Two subtrees tu, tv are merged by edge (u, v) if the merged tree tM satisfies radiustM (s) ≤ (1 + ε) R
u
v
tu
tv
tM

## Slide 11: BKRUS Algorithm (1/3)
u
v
tu
tv
Extension for upper bound constraint
  Two subtrees tu, tv are merged by edge (u, v) if the merged tree tM satisfies radiustM (s) ≤ (1 + ε) R
  Case 1 : If s ϵ tu
  disttu(S, u) + distG(u, v) + radiustv(v) ≤ (1 + ε) R
  Similar case for s ϵ tv

## Slide 12: BKRUS Algorithm (1/3)
Extension for upper bound constraint
  Two subtrees tu, tv are merged by edge (u, v) if the merged tree tM satisfies radiustM (s) ≤ (1 + ε) R
  Case 2 : If neither s ϵ tu nor s ϵ tv
  distG(S, x) + radiustM(x) ≤ (1 + ε) R
  If such x does not exist
  (u, v) is not feasible
u
v
tu
tv
x

## Slide 13: BKRUS Algorithm (2/3)
BKRUS maintains two matrices for tM
  P[V, V] denotes path lengths between (V, V) pairs
  r[V] denotes radii of every V
  (1). If s ϵ tu, tv, check : disttu(S, u) + distG(u, v) + radiustv(v) ≤ (1 + ε) R
  (2). Else, check : distG(S, x) + radiustM(x) ≤ (1 + ε) R, x ϵ tM

## Slide 14: BKRUS Algorithm (2/3)

## Slide 15: BKRUS Algorithm (3/3)
O(V)
O(V2) ONLY (V – 1) times
E times
Complexity = O(EV + V3)

## Slide 16: Extension to Elmore Delay Model
Elmore delay model is a more accurate delay estimation model on VLSI circuit
  Now, path delay is a
  function to driving
  network, not edge itself
So, new radii after each MERGE should be re-computed again
dist(x, y) is replaced by R(x, y)(C(x, y)/2 + CL)

## Slide 17: BKRUS Algorithm for Steiner Tree
A variation of BKRUS, named BKST
Hanan Grid

## Slide 18: Exact Algorithms – Gabow
Definition : T-exchange
  Given a pair of edges (e, f) where e ϵ T, f ϵ G \ T, and T \ e U f is a spanning tree, we define exchange of (e, f) has weight = w(f) – w(e)
Gabow’s Algorithm tries to find k smallest spanning trees evolved from original spanning tree with one exchange in every iteration
  Problem : Exponential Space Complexity (VV – 2)
  Solution : Once a feasible solution is found, return

## Slide 19: Exact Algorithms – Gabow
More on T-exchange
  If T is the minimum spanning tree, i.e. Cost(T) is the minimum among all spanning trees
    NO negative weight of exchange can be found
  Further, if (e, f) is the minimal T-exchange, T \ e U f is a spanning tree with the next smallest cost
In reality, some edges in original graph can be excluded at a preprocessing of Gabow’s algorithm (omitted here)

## Slide 20: Exact Algorithms – BKEX (1/2)
Motivation : Global Optimization
Definition : Negative-Sum-Exchange(s)
  A sequence of T-exchanges where sum of their weights are negative
BKEX starts from initial feasible solution, and reduce routing cost toward the optimal
  As a post-processing algorithm
  for, e.g. BKT

## Slide 21: Exact Algorithms – BKEX (2/2)
Complexity = O(En Vn+1)
depth = 0
depth = 1
depth = 2
depth = 3
depth = 4
depth = 5
y
x

## Slide 22: Heuristic from Exact Algorithms – BH2
BKT is a local minimum solution
  If an edge is rejected during the BKRUS algorithm, then that edge cannot become feasible at a later time (proof is omitted in the presentation)
  It can be shown BKT is a local optimum with respect to a single T-exchange
In order to jump out of local optimum, at least double T-exchanges are needed  BH2
  E.g. negative-sum-exchanges : +3, -5  -2
  Complexity = O(E2 V3)

## Slide 23: Upper and Lower Bounded MST
Sometimes we desire a spanning tree that consider both max and min distG(S, x) while minimizing routing cost
  For instance, clock skew in clock tree synthesis
Problem can be re-formulated as
  ε1 R ≤ radiusT (s) ≤ (1 + ε2)
  Some combinations of ε1, ε2 render NO solution
    However, for Steiner Trees, solutions may exist
How can BKRUS be extended now ?!

## Slide 24: Experiments – Tradeoff Curve

## Slide 25: Experiments – BH2 Improvements

## Slide 26: Experiments – Routing Cost Over MST
  Max = 2.711, 2.219, 2.056, 2.056
  Avg = 1.705, 1.517, 1.455, 1.452

## Slide 27: Conclusion and Future Work
Schemes for bounded path length minimal spanning tree with upper (and lower) bound control are presented
  With applications to , e.g. Elmore delay model
Two optimal algorithms
  BMST_G extends Gabow’s method
  BKEX using negative T-exchange technique
Heuristic BKRUS can be further enhanced with BKH2 as a post processing