## Slide 1: Codes and number systems
Introduction to Computer
Yung-Yu Chuang
with slides by Nisan & Schocken (www.nand2tetris.org) and Harris & Harris (DDCA)

## Slide 2: Coding
Assume that you want to communicate with your friend with a flashlight in a night, what will you do?
light painting?
What’s the problem?

## Slide 3: Solution #1
A: 1 blink
B: 2 blinks
C: 3 blinks
:
Z: 26 blinks
What’s the problem?
How are you? = 131 blinks

## Slide 4: Solution #2: Morse code
Hello

## Slide 5: Braille

## Slide 6: Braille

## Slide 7: What’s common in these codes?
They are both binary codes.

## Slide 8: Binary representations
Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.5V
2.8V
3.3V
0
1
0

## Slide 9: Number systems

## Slide 10
Decimal numbers
Binary numbers
Number Systems

## Slide 11
Decimal numbers
Binary numbers
Number Systems

## Slide 12: Binary numbers
Digits are 1 and 0
(a binary digit is called a bit)
1 = true
0 = false
MSB –most significant bit
LSB –least significant bit
Bit numbering:
A bit string could have different interpretations

## Slide 13
20 =
21 =
22 =
23 =
24 =
25 =
26 =
27 =
28 =
29 =
210 =
211 =
212 =
213 =
214 =
215 =
Powers of Two

## Slide 14
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
Handy to memorize up to 29
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two

## Slide 15: Unsigned binary integers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 16: Translating binary to decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Dn-1  2n-1) + (Dn-2  2n-2) + ... + (D1  21) + (D0  20)
D = binary digit
binary 00001001 = decimal 9:
(1  23) + (1  20) = 9

## Slide 17: Translating unsigned decimal to binary
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
37 = 100101

## Slide 18
Binary to decimal conversion:
  Convert 100112 to decimal
Decimal to binary conversion:
  Convert 4710 to binary
Number Conversion

## Slide 19
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 20
N-digit decimal number
  How many values?
  Range?
  Example: 3-digit decimal number:
N-bit binary number
  How many values?
  Range:
  Example: 3-digit binary number:
Binary Values and Range

## Slide 21
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 22: Integer storage sizes
Practice: What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 23
Bits
Bytes & Nibbles
Bytes
Bits, Bytes, Nibbles…

## Slide 24
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
Large Powers of Two

## Slide 25
What is the value of 224?
How many values can a 32-bit variable represent?
Estimating Powers of Two

## Slide 26
What is the value of 224?
- 24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
-22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 27: Large measurements
Kilobyte (KB), 210 bytes
Megabyte (MB), 220 bytes
Gigabyte (GB), 230 bytes
Terabyte (TB), 240 bytes
Petabyte
Exabyte
Zettabyte
Yottabyte

## Slide 28
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 
1 | 1 | 
2 | 2 | 
3 | 3 | 
4 | 4 | 
5 | 5 | 
6 | 6 | 
7 | 7 | 
8 | 8 | 
9 | 9 | 
A | 10 | 
B | 11 | 
C | 12 | 
D | 13 | 
E | 14 | 
F | 15 | 
Hexadecimal Numbers

## Slide 29
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111
Hexadecimal Numbers

## Slide 30
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 31: Translating binary to hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 000101101010011110010100 to hexadecimal:

## Slide 32: Converting hexadecimal to decimal
Multiply each digit by its corresponding power of 16:
  dec = (D3  163) + (D2  162) + (D1  161) + (D0  160)
Hex 1234 equals (1  163) + (2  162) + (3  161) + (4  160), or decimal 4,660.
Hex 3BA4 equals (3  163) + (11 * 162) + (10  161) + (4  160), or decimal 15,268.

## Slide 33
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
Hexadecimal to decimal conversion:
  Convert 0x4AF to decimal
Hexadecimal to Binary Conversion

## Slide 34
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 35: Powers of 16
Used when calculating hexadecimal values up to 8 digits long:

## Slide 36: Converting decimal to hexadecimal
decimal 422 = 1A6 hexadecimal

## Slide 37
Decimal
Binary
Addition

## Slide 38
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 39
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Overflow!
Binary Addition Examples

## Slide 40
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 41: Hexadecimal addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 42
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 43: Signed integers
The highest bit indicates the sign. 1 = negative, 0 = positive
If the highest digit of a hexadecmal integer is > 7, the value is negative. Examples: 8A, C5, A2, 9D

## Slide 44
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 =
- 6 =
Range of an N-bit sign/magnitude number:
Sign/Magnitude Numbers

## Slide 45
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 46
Problems:
  Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
  Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 47
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 48: Two's complement notation
Steps:
  Complement (reverse) each bit
  Add 1
Note that 00000001 + 11111111 = 00000000

## Slide 49
Flip the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
“Taking the Two’s Complement”

## Slide 50
Flip the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
“Taking the Two’s Complement”

## Slide 51
Take the two’s complement of 610 = 01102
What is the decimal value of 10012?
Two’s Complement Examples

## Slide 52
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 53: Binary subtraction
When subtracting A – B, convert B to its two's complement
Add A to (–B)
0 1 0 1 0 0 1 0 1 0
– 0 1 0 1 1 1 0 1 0 1
1 1 1 1 1
Advantages for 2’s complement:
No two 0’s
Sign bit
Remove the need for separate circuits for add and sub

## Slide 54
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 55
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 56
b = 1-b
a = 111…1 – a = (2N-1)-a
a +1= 2N-a
In 2’s complement, 2N-a is used to represent –a since 2N-a ≡ -a (mod 2N)
Two’s Complement

## Slide 57
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 58
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 59
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 00112 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 60
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 61: Ranges of signed integers
The highest bit is reserved for the sign. This limits the range:

## Slide 62: Character
Character sets
  Standard ASCII (0 – 127)
  Extended ASCII (0 – 255)
  ANSI (0 – 255)
  Unicode (0 – 65,535)
Null-terminated String
  Array of characters followed by a null byte
Using the ASCII table
  back inside cover of book

## Slide 64: Representing Instructions
int sum(int x, int y)
{
return x+y;
}
Different machines use totally different
instructions and encodings
  For this example, Alpha & Sun use two 4-byte instructions
    Use differing numbers of instructions in other cases
  PC uses 7 instructions with lengths 1, 2, and 3 bytes
    Same for NT and for Linux
    NT / Linux not fully binary compatible
E5
8B
55
89
PC sum
45
0C
03
45
08
89
EC
5D
C3
00
00
30
42
Alpha sum
01
80
FA
6B
E0
08
81
C3
Sun sum
90
02
00
09