## Slide 1: Machine (Assembly) Language
www.nand2tetris.org
Building a Modern Computer From First Principles
Notes: 1

## Slide 2: Where we are at:
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12

## Slide 3: Machine language
Abstraction – implementation duality:
Machine language ( = instruction set) can be viewed as a programmer-oriented abstraction of the hardware platform
The hardware platform can be viewed as a physical means for realizing the machine language abstraction

## Slide 4: Machine language
Abstraction – implementation duality:
Machine language ( = instruction set) can be viewed as a programmer-oriented abstraction of the hardware platform
The hardware platform can be viewed as a physical means for realizing the machine language abstraction
Another duality:
Binary version: 0001 0001 0010 0011 (machine code)
Symbolic version ADD R1, R2, R3 (assembly)

## Slide 5: Machine language
Abstraction – implementation duality:
Machine language ( = instruction set) can be viewed as a programmer-oriented abstraction of the hardware platform
The hardware platform can be viewed as a physical means for realizing the machine language abstraction
Another duality:
Binary version
Symbolic version
Loose definition:
Machine language = an agreed-upon formalism for manipulating a memory using a processor and a set of registers
Same spirit but different syntax across different hardware platforms.
ALU
combinational
Memory
state

## Slide 6: Lecture plan
Machine languages at a glance
The Hack machine language:
  Symbolic version
  Binary version
Perspective
(The assembler will be covered in chapter 6).

## Slide 7: Typical machine language commands (3 types)
ALU operations
Memory access operations
(addressing mode: how to specify operands)
  Immediate addressing, LDA R1, 67 // R1=67
  Direct addressing, LD R1, 67 // R1=M[67]
  Indirect addressing, LDI R1, R2 // R1=M[R2]
Flow control operations

## Slide 8: Typical machine language commands (a small sample)
// In what follows R1,R2,R3 are registers, PC is program counter,
// and addr is some value.
ADD R1,R2,R3 // R1  R2 + R3
ADDI R1,R2,addr // R1  R2 + addr
AND R1,R1,R2 // R1  R1 and R2 (bit-wise)
JMP addr // PC  addr
JEQ R1,R2,addr // IF R1 == R2 THEN PC  addr ELSE PC++
LOAD R1, addr // R1  RAM[addr]
STORE R1, addr // RAM[addr]  R1
NOP // Do nothing
// Etc. – some 50-300 command variants

## Slide 9: The Hack computer
A 16-bit machine consisting of the following elements:

## Slide 10: The Hack computer
The ROM is loaded with a Hack program
The reset button is pushed
The program starts running

## Slide 11: The Hack computer
A 16-bit machine consisting of the following elements:
Both memory chips are 16-bit wide and have 15-bit address space.

## Slide 12: The Hack computer (CPU)
A 16-bit machine consisting of the following elements:

## Slide 13: The Hack computer
A 16-bit machine consisting of the following elements:
Data memory: RAM – an addressable sequence of registers
Instruction memory: ROM – an addressable sequence of registers
Registers: D, A, M, where M stands for RAM[A]
Processing: ALU, capable of computing various functions
Program counter: PC, holding an address
Control: The ROM is loaded with a sequence of 16-bit instructions, one per memory location, beginning at address 0. Fetch-execute cycle: later
Instruction set: Two instructions: A-instruction, C-instruction.

## Slide 14: The A-instruction
@value // A  value
Where value is either a number or a symbol referring to some number.
Why A-instruction?
Example:
@21
Effect:
Sets the A register to 21
RAM[21] becomes the selected RAM register M
In TOY, we store address in the instruction (fmt #2). But, it is impossible to pack a 15-bit address into a 16-bit instruction. So, we have the A-instruction for setting addresses if needed.

## Slide 15: The A-instruction
@value // A  value
Used for:
Entering a constant value ( A = value)
@17 // A = 17
D = A // D = 17
Coding example:
@17 // A = 17
D = M // D = RAM[17]
M = -1 // RAM[17]=-1
Selecting a RAM location ( register = RAM[A])
@17 // A = 17
JMP // fetch the instruction
// stored in ROM[17]
Selecting a ROM location ( PC = A )

## Slide 16: The C-instruction
dest = comp ; jump
Both dest and jump are optional.
First, we compute something.
Next, optionally, we can store the result, or use it to jump to somewhere to continue the program execution.
0, 1, -1, D, A, !D, !A, -D, -A, D+1, A+1, D-1, A-1, D+A, D-A, A-D, D&A, D|A
M, !M, -M, M+1, M-1, D+M, D-M, M-D, D&M, D|M
comp:
dest: null, A, D, M, MD, AM, AD, AMD
jump: null, JGT, JEQ, JLT, JGE, JNE, JLE, JMP
Compare to zero. If the condition holds, jump to ROM[A]

## Slide 17: The C-instruction
dest = comp ; jump
Computes the value of comp
Stores the result in dest
If (the condition jump compares to zero is true), goto the instruction at ROM[A].

## Slide 18: The C-instruction
dest = comp ; jump
Example: set the D register to -1
D = -1
Example: set RAM[300] to the value of the D register minus 1
@300
M = D-1
Example: if ((D-1) == 0) goto ROM[56]
@56
D-1; JEQ
comp:
dest: null, A, D, M, MD, AM, AD, AMD
jump: null, JGT, JEQ, JLT, JGE, JNE, JLE, JMP
0, 1, -1, D, A, !D, !A, -D, -A, D+1, A+1, D-1, A-1, D+A, D-A, A-D, D&A, D|A
M, !M, -M, M+1, M-1, D+M, D-M, M-D, D&M, D|M

## Slide 19: Hack programming reference card
Hack commands:
A-command: @value // set A to value
C-command: dest = comp ; jump // dest = and ;jump // are optional
Where:
comp =
0 , 1 , -1 , D , A , !D , !A , -D , -A , D+1 , A+1 , D-1, A-1 , D+A , D-A , A-D , D&A , D|A,
M , !M , -M , M+1, M-1 , D+M, D-M, M-D, D&M, D|M
dest = M, D, A, MD, AM, AD, AMD, or null
jump = JGT , JEQ , JGE , JLT , JNE , JLE , JMP, or null
In the command dest = comp; jump, the jump materialzes if (comp jump 0) is true. For example, in D=D+1,JLT, we jump if D+1 < 0.

## Slide 20: The Hack machine language
Two ways to express the same semantics:
Binary code (machine language)
Symbolic language (assembly)
@17
D+1; JLE
symbolic
0000 0000 0001 0001
1110 0111 1100 0110
binary
translate
execute
hardware

## Slide 21: The A-instruction
@value
value is a non-negative decimal number <= 215-1 or
A symbol referring to such a constant
0value
value is a 15-bit binary number
symbolic
binary
@21
0000 0000 0001 0101
Example

## Slide 22: The C-instruction
dest = comp ; jump
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
symbolic
binary
opcode
]
not used
comp
dest
jump

## Slide 23: The C-instruction
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
comp
dest
jump

## Slide 24: The C-instruction
A D M
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
comp
dest
jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]

## Slide 25: The C-instruction
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
comp
dest
jump
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
< = >

## Slide 26
We will focus on writing the assembly code.
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
0000000000000001
1110001100001000
0000000000010110
1110101010000111
Target code
assemble
Hack assembly/machine language
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)
Hack assembler
or CPU emulator

## Slide 27: Working with registers and memory
D: data register
A: address/data register
M: the currently selected memory cell, M=RAM[A]
address
ROM
Instruction memory
out
RAM
address
Data memory
out
Address register
Data register
A
...
32766
32767
...
32766
32767
0
1
2
...
0
1
2
...
M
instruction
D

## Slide 28: Hack programming exercises
Exercise: Implement the following tasks using Hack commands:
Set D to A-1
Set both A and D to A + 1
Set D to 19
D++
D=RAM[17]
Set RAM[5034] to D - 1
Set RAM[53] to 171
Add 1 to RAM[7], and store the result in D.

## Slide 29: Hack programming exercises
Exercise: Implement the following tasks using Hack commands:
Set D to A-1
Set both A and D to A + 1
Set D to 19
D++
D=RAM[17]
Set RAM[5034] to D - 1
Set RAM[53] to 171
Add 1 to RAM[7], and store the result in D.
1. D = A-1
2. AD=A+1
3. @19
D=A
4. D=D+1
5. @17
D=M
6. @5034
M=D-1
7. @171
D=A
@53
M=D
8. @7
D=M+1

## Slide 30: A simple program: add two numbers (demo)
// Computes: RAM[2] = RAM[0] + RAM[1]
// D = RAM[0]
@0
D=M
// D = D + RAM[1]
@1
D=D+M
// RAM[2] = D
@2
M=D
Add.asm (example)
When loading a symbolic program into the CPU emulator, the emulator translates it into binary code (using a built-in assembler)
Execute
Load into the CPU emulator
0000000000000000
1000010010001101
0000000000000001
1010011001100001
0000000000000010
1110010010010011
Binary

## Slide 31: Terminate properly
To avoid malicious code, you could terminate your program with an infinite loop, such as
@6
0; JMP
00: @0
01: D=M
02: @1
03: D=D+M
04: @2
05: M=D

## Slide 32: Built-in symbols
symbol | value
R0 | 0
R1 | 1
R2 | 2
… | …
R15 | 15
SCREEN | 16384
KBD | 24576
symbol | value
SP | 0
LCL | 1
ARG | 2
THIS | 3
THAT | 4
R0, R1, …, R15 : virtual registers
SCREEN and KBD : base address of I/O memory maps
Others: used in the implementation of the Hack Virtual Machine
Note that Hack assembler is case-sensitive, R5 != r5

## Slide 33: Branching
// Program: branch.asm
// if R0>0
// R1=1
// else
// R1=0

## Slide 34: Branching
// Program: branch.asm
// if R0>0
// R1=1
// else
// R1=0
@R0
D=M // D=RAM[0]
@8
D; JGT // If R0>0 goto 8
@R1
M=0 // R1=0
@10
0; JMP // go to end
@R1
M=1 // R1=1
@10
0; JMP

## Slide 35: Branching
// Program: branch.asm
// if R0>0
// R1=1
// else
// R1=0
@R0
D=M // D=RAM[0]
@8
D; JGT // If R0>0 goto 8
@R1
M=0 // R1=0
@10
0; JMP // go to end
@R1
M=1 // R1=1
@10
0; JMP

## Slide 36: Branching with labels
// Program: branch.asm
// if R0>0
// R1=1
// else
// R1=0
@R0
D=M // D=RAM[0]
@POSTIVE
D; JGT // If R0>0 goto 8
@R1
M=0 // R1=0
@END
0; JMP // go to end
(POSTIVE)
@R1
M=1 // R1=1
(END)
@10
0; JMP
declare a label
refer a label
@0
D=M
@8
D;JGT
@1
M=0
@10
0;JMP
@1
M=1
@10
0; JMP
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16

## Slide 37: IF logic – Hack style
if condition {
code block 1
} else {
code block 2
}
code block 3
High level:
D  condition
@IF_TRUE
D;JEQ
code block 2
@END
0;JMP
(IF_TRUE)
code block 1
(END)
code block 3
Hack:
Hack convention:
True is represented by -1
False is represented by 0

## Slide 38: Coding examples (practice)
Exercise: Implement the following tasks using Hack commands:
goto 50
if D==0 goto 112
if D<9 goto 507
if RAM[12] > 0 goto 50
if sum>0 goto END
if x[i]<=0 goto NEXT.

## Slide 39: Coding examples (practice)
Exercise: Implement the following tasks using Hack commands:
goto 50
if D==0 goto 112
if D<9 goto 507
if RAM[12] > 0 goto 50
if sum>0 goto END
if x[i]<=0 goto NEXT.
1. @50
0; JMP
2. @112
D; JEQ
3. @9
D=D-A
@507
D; JLT
4. @12
D=M
@50
D; JGT
5. @sum
D=M
@END
D: JGT
6. @i
D=M
@x
A=D+M
D=M
@NEXT
D; JLE

## Slide 40: variables
// Program: swap.asm
// temp = R1
// R1 = R0
// R0 = temp

## Slide 41: variables
// Program: swap.asm
// temp = R1
// R1 = R0
// R0 = temp
@R1
D=M
@temp
M=D // temp = R1
@R0
D=M
@R1
M=D // R1 = R0
@temp
D=M
@R0
M=D // R0 = temp
(END)
@END
0;JMP
When a symbol is encountered, the assembler looks up a symbol table
If it is a new label, assign a number (address of the next available memory cell) to it.
For this example, temp is assigned with 16.
If the symbol exists, replace it with the number recorded in the table.
With symbols and labels, the program is easier to read and debug. Also, it can be relocated.

## Slide 42: Hack program (exercise)
Exercise: Implement the following tasks using Hack commands:
sum = 0
j = j + 1
q = sum + 12 – j
arr[3] = -1
arr[j] = 0
arr[j] = 17

## Slide 43: Hack program (exercise)
Exercise: Implement the following tasks using Hack commands:
sum = 0
j = j + 1
q = sum + 12 – j
arr[3] = -1
arr[j] = 0
arr[j] = 17
1. @sum
M=0
2. @j
M=M+1
3. @sum
D=M
@12
D=D+A
@j
D=D-M
@q
M=D
4. @arr
D=M
@3
A=D+A
M=-1
5. @j
D=M
@arr
A=D+M
M=0
6. @j
D=M
@arr
D=D+M
@ptr
M=D
@17
D=A
@ptr
A=M
M=D

## Slide 44: WHILE logic – Hack style
while condition {
code block 1
}
Code block 2
High level:
(LOOP)
D  condition
@END
D;JNE
code block 1
@LOOP
0;JMP
(END)
code block 2
Hack:
Hack convention:
True is represented by -1
False is represented by 0

## Slide 45: Complete program example
// Adds 1+...+100.
int i = 1;
int sum = 0;
while (i <= 100){
sum += i;
i++;
}
C language code:
Hack assembly convention:
Variables: lower-case
Labels: upper-case
Commands: upper-case

## Slide 46: Complete program example
i = 1;
sum = 0;
LOOP:
if (i>100) goto END
sum += i;
i++;
goto LOOP
END:
Pseudo code:
// Adds 1+...+100.
@i // i refers to some RAM location
M=1 // i=1
@sum // sum refers to some RAM location
M=0 // sum=0
(LOOP)
@i
D=M // D = i
@100
D=D-A // D = i - 100
@END
D;JGT // If (i-100) > 0 goto END
@i
D=M // D = i
@sum
M=D+M // sum += i
@i
M=M+1 // i++
@LOOP
0;JMP // Got LOOP
(END)
@END
0;JMP // Infinite loop
Hack assembly code:
Demo
CPU emulator
Hack assembly convention:
Variables: lower-case
Labels: upper-case
Commands: upper-case

## Slide 47: Example
// for (i=0; i<n; i++)
// arr[i] = -1;
Pseudo code:

## Slide 48: Example
// for (i=0; i<n; i++)
// arr[i] = -1;
Pseudo code:
i = 0
(LOOP)
if (i-n)>=0 goto END
arr[i] = -1
i++
goto LOOP
(END)

## Slide 49: Example
// for (i=0; i<n; i++)
// arr[i] = -1;
@i
M=0
(LOOP)
@i
D=M
@n
D=D-M
@END
D; JGE
@arr
D=M
@i
A=D+M
M=-1
@i
M=M+1
@LOOP
0; JMP
(END)
Pseudo code:
i = 0
(LOOP)
if (i-n)>=0 goto END
arr[i] = -1
i++
goto LOOP
(END)

## Slide 50: Perspective
Hack is a simple machine language
User friendly syntax: D=D+A instead of ADD D,D,A
Hack is a “½-address machine”: any operation that needs to operate on the RAM must be specified using two commands: an A-command to address the RAM, and a subsequent C-command to operate on it
A Macro-language can be easily developed
  D=D+M[XXX] => @XXX followed by D=D+M
  GOTO YYY => @YYY followed by 0; JMP
A Hack assembler is needed and will be discusses and developed later in the course.