## Slide 1: Arithmetic Logic Unit (ALU)
Introduction to Computer
Yung-Yu Chuang
with slides by Sedgewick & Wayne (introcs.cs.princeton.edu), Nisan & Schocken (www.nand2tetris.org) and Harris & Harris (DDCA)

## Slide 2: Let's Make an Adder Circuit
Goal. x + y = z for 4-bit integers.
  We build 4-bit adder: 9 inputs, 4 outputs.
  Same idea scales to 128-bit adder.
  Key computer component.
8
4
2
7
7
5
3
9
+
6
0
6
6
1
1
1
0
Notes: We treat 4 Boolean variables as a singe 4-bit binary integer.
Ignore c0 (carry into bit 0) for now

## Slide 3
no overflow
overflow
Algorithm: exactly the same as in decimal addition
Overflow (MSB carry) has to be dealt with.
Binary addition
Assuming a 4-bit system:
0 0 0 1
1 0 0 1
0 1 0 1
0 1 1 1 0
+
1 1 1 1
1 0 1 1
0 1 1 1
1 0 0 1 0
+

## Slide 4: Representing negative numbers (4-bit system)
The codes of all positive numbers begin with a “0”
The codes of all negative numbers begin with a “1“
To convert a number: leave all trailing 0’s and first 1 intact, and flip all the remaining bits
0 0000
1 0001 1111 -1
2 0010 1110 -2
3 0011 1101 -3
4 0100 1100 -4
5 0101 1011 -5
6 0110 1010 -6
7 0111 1001 -7
1000 -8
Example: 2 - 5 = 2 + (-5) = 0 0 1 0
+ 1 0 1 1
1 1 0 1 = -3

## Slide 5: Let's Make an Adder Circuit
Step 1. Represent input and output in binary.
x1
x2
x3
x0
y1
y2
y3
y0
+
z1
z2
z3
z0
1
0
0
0
1
1
0
1
+
0
0
1
1
0
1
1
0
Notes: We treat 4 Boolean variables as a singe 4-bit binary integer.
Ignore c0 (carry into bit 0) for now

## Slide 6: Let's Make an Adder Circuit
Goal. x + y = z for 4-bit integers.
Step 2. [first attempt]
  Build truth table.
Q. Why is this a bad idea?
A. 128-bit adder: 2256+1 rows >> # electrons in universe!
x1
x2
x3
x0
y1
y2
y3
y0
+
z1
z2
z3
z0
4-Bit Adder Truth Table
y2
y3
0
0
0
0
1
.
1
0
0
0
0
0
.
1
x0
x1
0
0
0
0
0
.
1
0
0
0
0
0
.
1
x2
x3
0
0
0
0
0
.
1
0
0
0
0
0
.
1
y0
y1
0
1
0
1
0
.
1
0
0
1
1
0
.
1
z2
z3
0
0
0
0
1
.
1
0
0
0
0
0
.
1
z0
z1
0
1
0
1
0
.
1
0
0
1
1
0
.
1
28+1 = 512 rows!
c0
0
0
0
0
0
.
1
cin
cout
Notes: Building truth table is a bit unwieldy. If N = 128 bit adder, then 2^256 ~ 10^77 rows.
10^77 electrons in universe
Would produces very large circuit => try to do something more clever.
Use abstraction to break down problem.

## Slide 7: 1-bit half adder
x
y
s
c
ADD
x
y
c
s
We add numbers one bit at a time.

## Slide 8: 1-bit full adder
x
y
s
ADD
x
Cout
Cin
y
s
Cout
Cin

## Slide 9: 8-bit adder

## Slide 10: Let's Make an Adder Circuit
Goal. x + y = z for 4-bit integers.
Step 2. [do one bit at a time]
  Build truth table for carry bit.
  Build truth table for summand bit.
x1
x2
x3
x0
y1
y2
y3
y0
+
z1
z2
z3
z0
c1
c2
c3
c0 = 0
Carry Bit
ci
ci+1
yi
xi
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
Summand Bit
ci
zi
yi
xi
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
cout
Notes: Start by building circuit for one bit only.
Not a bit-by-bit function of inputs because of "carry".

## Slide 11: Let's Make an Adder Circuit
Goal. x + y = z for 4-bit integers.
Step 3.
  Derive (simplified) Boolean expression.
MAJ
0
0
0
1
0
1
1
1
ODD
0
1
1
0
1
0
0
1
ci
ci+1
yi
xi
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
ci
zi
yi
xi
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
Carry Bit
Summand Bit

## Slide 12: Let's Make an Adder Circuit
Goal. x + y = z for 4-bit integers.
Step 4.
  Transform Boolean expression into circuit.
  Chain together 1-bit adders.
Notes: "flows" from right to left

## Slide 13: Adder: Interface

## Slide 14: Adder: Component Level View

## Slide 15: Adder: Switch Level View

## Slide 16: Marble adding machine

## Slide 17: Subtractor
Subtractor circuit: z = x – y.
  One approach: design like adder circuit

## Slide 18: Subtractor
Subtractor circuit: z = x – y.
  One approach: design like adder circuit
  Better idea: reuse adder circuit
    2’s complement: to negate an integer, flip bits, then add 1

## Slide 19: Subtractor
Subtractor circuit: z = x – y.
  One approach: design like adder circuit
  Better idea: reuse adder circuit
    2’s complement: to negate an integer, flip bits, then add 1

## Slide 20: Put adder and subtractor together

## Slide 21: Shifter
4-bit Shifter
SHIFT
s0
s1
s2
s3
z0
z1
z2
z3
x0
x1
x2
x3
Only one of them will be on at a time.
Notes: Give formula???

## Slide 22: Shifter
 | z3 | z2 | z1 | z0
s0 |  |  |  | 
s1 |  |  |  | 
s2 |  |  |  | 
s3 |  |  |  | 

## Slide 23: Shifter
 | z3 | z2 | z1 | z0
s0 | x3 | x2 | x1 | x0
s1 | x2 | x1 | x0 | 0
s2 | x1 | x0 | 0 | 0
s3 | x0 | 0 | 0 | 0
z0 = s0‧x0 + s1‧0 + s2‧0 + s3‧0
z1 = s0‧x1 + s1‧x0 + s2‧0 + s3‧0
z2 = s0‧x2 + s1‧x1 + s2‧x0 + s3‧0
z3 = s0‧x3 + s1‧x2 + s2‧x1 + s3‧x0

## Slide 24: Shifter
z0 = s0‧x0 + s1‧0 + s2‧0 + s3‧0
z1 = s0‧x1 + s1‧x0 + s2‧0 + s3‧0
z2 = s0‧x2 + s1‧x1 + s2‧x0 + s3‧0
z3 = s0‧x3 + s1‧x2 + s2‧x1 + s3‧x0
Notes: Give formula???

## Slide 25: N-bit Decoder
N-bit decoder
  N address inputs, 2N data outputs
  Addresses output bit is 1;
  all others are 0

## Slide 26: N-bit Decoder
N-bit decoder
  N address inputs, 2N data outputs
  Addresses output bit is 1;
  all others are 0

## Slide 27: 2-Bit Decoder Controlling 4-Bit Shifter
Ex. Put in a binary amount to shift.
r0r1

## Slide 28: Arithmetic Logic Unit
Arithmetic logic unit (ALU). Computes all operations in parallel.
  Add and subtract.
  Xor.
  And.
  Shift left or right.
Q. How to select desired answer?
Notes: also get a free "add-1" instruction. Useful for i++.

## Slide 29: 1 Hot OR
adder
xor
shift
decoder
x．1 = x
x．0 = 0
x + 0 = x

## Slide 30: 1 Hot OR
1 hot OR.
  All devices compute their answer; we pick one.
  Exactly one select line is on.
  Implies exactly one output line is relevant.
adder
xor
shifter
x．1 = x
x．0 = 0
x + 0 = x
Notes: mathematician might say we're done since, in principle can build TOY computer with finite amount of resources
engineer wants to build it more efficiently, needs new abstractions
Note: 4080 inputs assumes all registers = 0 initially, mem[FF] not used and and pc = 10. (Does not include stdin) there are 4096+16+1 outputs plus possibility of infinite loop plus stdout.

## Slide 31: Bus
16-bit bus
  Bundle of 16 wires
  Memory transfer
  Register transfer
8-bit bus
  Bundle of 8 wires
  TOY memory address
4-bit bus
  Bundle of 4 wires
  TOY register address

## Slide 32: Bitwise AND, XOR, NOT
Bitwise logical operations
  Inputs x and y: n bits each
  Output z: n bits
  Apply logical operation to each corresponding pair of bits

## Slide 33: TOY ALU
TOY ALU
  Big combinational logic
  16-bit bus
  Add, subtract, and, xor, shift left, shift right, copy input 2

## Slide 34: Device Interface Using Buses
Device. Processes a word at a time.
Input bus. Wires on top.
Output bus. Wires on bottom.
Control. Individual wires on side.
16-bit words for TOY memory
Notes: mathematician might say we're done since, in principle can build TOY computer with finite amount of resources
engineer wants to build it more efficiently, needs new abstractions
Note: 4080 inputs assumes all registers = 0 initially, mem[FF] not used and and pc = 10. (Does not include stdin) there are 4096+16+1 outputs plus possibility of infinite loop plus stdout.

## Slide 35: ALU
Arithmetic logic unit.
  Add and subtract.
  Xor.
  And.
  Shift left or right.
Arithmetic logic unit.
  Computes all operations in parallel.
  Uses 1-hot OR to pick each bit answer.
How to convert opcode to
1-hot OR signal?
Notes: also get a free "add-1" instruction. Useful for i++.

## Slide 38: The ALU in the CPU context
PC
Registers
W
W Data
A Data
B Data
W Addr
A Addr
B Addr
+
1-bit
counter
1
5
2
4
=0
>0
Opcode
Execute
Fetch
Clock
Memory
W
W Data
Addr
R Data
IR
op
d
s
t
Cond
Eval
A
L
U
Control
Clock
1
0
1
0
0
1
1
0
10
01
00

## Slide 39: Hack ALU
out(x, y, control bits) =
x+y, x-y, y–x,
0, 1, -1,
x, y, -x, -y,
x!, y!,
x+1, y+1, x-1, y-1,
x&y, x|y
control bits
flags

## Slide 40: Hack ALU
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 41: Hack ALU
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 42: Hack ALU
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 43: Hack ALU
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 44: Hack ALU
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 45: Hack ALU
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=

## Slide 46: Hack ALU
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y

## Slide 47: Hack ALU: !x
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y

## Slide 48: Hack ALU: !x
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute !x
x: 1 1 0 0
y: 1 0 1 1 (irrelevant)
Following pre-setting:
x: 1 1 0 0
y: 1 1 1 1
Computation and post-setting:
x&y: 1 1 0 0
!(x&y): 0 0 1 1 (!x)

## Slide 49: Hack ALU: x|y
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute x|y
x: 0 1 0 1
y: 0 0 1 1
Following pre-setting:
x: 1 0 1 0
y: 1 1 0 0
Computation and post-setting:
x&y: 1 0 0 0
!(x&y): 0 1 1 1

## Slide 50: Hack ALU: y-1
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute y-1
x: 0 1 0 1 (irrelevant)
y: 0 1 1 0 (6)
Following pre-setting:
x: 1 1 1 1
y: 0 1 1 0
Computation and post-setting:
x+y: 0 1 0 1
x+y: 0 1 0 1 (5)

## Slide 51: Hack ALU: y-x
pre-setting the x input |  | pre-setting the y input |  | selecting between computing + or & | post-setting the output | Resulting ALU output
zx | nx | zy | ny | f | no | out
if zx then x=0 | if nx then x=!x | if zy then y=0 | if ny then y=!y | if f then out=x+y else out=x&y | if no then out=!out | out(x,y)=
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | -1
0 | 0 | 1 | 1 | 0 | 0 | x
1 | 1 | 0 | 0 | 0 | 0 | y
0 | 0 | 1 | 1 | 0 | 1 | !x
1 | 1 | 0 | 0 | 0 | 1 | !y
0 | 0 | 1 | 1 | 1 | 1 | -x
1 | 1 | 0 | 0 | 1 | 1 | -y
0 | 1 | 1 | 1 | 1 | 1 | x+1
1 | 1 | 0 | 1 | 1 | 1 | y+1
0 | 0 | 1 | 1 | 1 | 0 | x-1
1 | 1 | 0 | 0 | 1 | 0 | y-1
0 | 0 | 0 | 0 | 1 | 0 | x+y
0 | 1 | 0 | 0 | 1 | 1 | x-y
0 | 0 | 0 | 1 | 1 | 1 | y-x
0 | 0 | 0 | 0 | 0 | 0 | x&y
0 | 1 | 0 | 1 | 0 | 1 | x¦y
Example: compute y-x
x: 0 1 0 1 (5)
y: 0 1 1 0 (6)
Following pre-setting:
x: 0 1 0 1
y: 1 0 0 1
Computation and post-setting:
x+y: 1 1 1 0
!(x+y): 0 0 0 1 (1)

## Slide 52
The ALU in the CPU context (a sneak preview of the Hack platform)
ALU
Mux
D
out
A/M
a
D register
A register
A
M
c1,c2, … ,c6
RAM
(selected register)

## Slide 53
www.nand2tetris.org
Project 2

## Slide 54
Project 2
Given: All the chips built in Project 1
HalfAdder
FullAdder
Add16
Inc16
ALU
Goal: Build the chips:

## Slide 55
Half Adder
a | b | sum | carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
/** Computes the sum of two bits. */
CHIP HalfAdder {
IN a, b;
OUT sum, carry;
PARTS:
// Put your code here:
}
HalfAdder.hdl
Implementation tip
Can be built from two gates built in project 1.

## Slide 56
Full Adder
Implementation tip
Can be built from two half-adders.
/** Computes the sum of three bits. */
CHIP FullAdder {
IN a, b, c;
OUT sum, carry;
PARTS:
// Put your code here:
}
FullAdder.hdl
a | b | c | sum | carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 57
/* Adds two 16-bit, two’s-complement values. The most-significant carry bit is ignored. */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
// Put you code here:
}
Add16.hdl
The bitwise additions are done in parallel
The carry propagation is sequential
Yet… it works fine, as is.
Implementation note
If you need to set a pin x to 0 (or 1) in HDL, use: x = false (or x = true)
16-bit Adder

## Slide 58
16-bit incrementor
Inc16.hdl
Implementation:
Simple.
/** Outputs in + 1. */
CHIP Inc16 {
IN in[16];
OUT out[16];
PARTS:
// Put you code here:
}

## Slide 59
ALU

## Slide 60
ALU.hdl
/** The ALU */
// Manipulates the x and y inputs as follows:
// if (zx == 1) sets x = 0 // 16-bit true
// if (nx == 1) sets x = !x // 16-bit Not
// if (zy == 1) sets y = 0 // 16-bit true
// if (ny == 1) sets y = !y // 16-bit Not
// if (f == 1) sets out = x + y // 2's-complement addition
// if (f == 0) sets out = x & y // 16-bit And
// if (no == 1) sets out = !out // 16-bit Not
// if (out == 0) sets zr = 1 // 1-bit true
// if (out < 0) sets ng = 1 // 1-bit true
...
ALU

## Slide 61
ALU
ALU.hdl
Implementation tips
We need logic for:
Implementing “if bit == 0/1” conditions
Setting a 16-bit value to 0000000000000000
Setting a 16-bit value to 1111111111111111
Negating a 16-bit value (bitwise)
Computing Add and And on two 16-bit values
Implementation strategy
Start by building an ALU that computes out
Next, extend it to also compute zr and ng.
/** The ALU */
// Manipulates the x and y inputs as follows:
// if (zx == 1) sets x = 0 // 16-bit true
// if (nx == 1) sets x = !x // 16-bit Not
// if (zy == 1) sets y = 0 // 16-bit true
// if (ny == 1) sets y = !y // 16-bit Not
// if (f == 1) sets out = x + y // 2's-complement addition
// if (f == 0) sets out = x & y // 16-bit And
// if (no == 1) sets out = !out // 16-bit Not
// if (out == 0) sets zr = 1 // 1-bit true
// if (out < 0) sets ng = 1 // 1-bit true
...

## Slide 62
Using multi-bit truth / false constants:
...
// Suppose that x, y, z are 8-bit bus-pins:
5
4
7
6
1
0
3
2
x:
y:
z:
Relevant bus tips

## Slide 63
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
5
4
7
6
1
0
3
2
x:
y:
z:
Using multi-bit truth / false constants:
Relevant bus tips

## Slide 64
5
4
7
6
1
0
3
2
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
y:
z:
1
1
1
1
1
1
1
1
x:
Using multi-bit truth / false constants:
Relevant bus tips

## Slide 65
5
4
7
6
1
0
3
2
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
z:
1
1
1
1
1
1
1
1
x:
0
0
0
0
0
0
0
0
y:
Using multi-bit truth / false constants:
Relevant bus tips

## Slide 66
...
// Suppose that x, y, z are 8-bit bus-pins:
chipPart(..., x = true, y = false, z[0..2] = true, z[6..7] = true);
...
Unassigned bits are set to 0
5
4
7
6
1
0
3
2
1
1
1
1
1
1
1
1
x:
0
0
0
0
0
0
0
0
y:
0
0
1
1
1
1
0
1
z:
Using multi-bit truth / false constants:
We can assign values to sub-buses
Relevant bus tips

## Slide 67
Sub-bussing:
We can assign n-bit values to sub-buses, for any n
We can create n-bit bus pins, for any n
/* 16-bit adder */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
CHIP Foo {
IN x[8], y[8], z[16]
OUT out[16]
PARTS
...
Add16 (a[0..7] = x, a[8..15] = y, b = z, out = …);
...
Add16 (a = …, b = …, out[0..3] = t1, out[4..15] = t2);
...
}
Relevant bus tips

## Slide 68
/* 16-bit adder */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
CHIP Foo {
IN x[8], y[8], z[16]
OUT out[16]
PARTS
...
Add16 (a[0..7] = x, a[8..15] = y, b = z, out = …);
...
Add16 (a = …, b = …, out[0..3] = t1, out[4..15] = t2);
...
}
Sub-bussing:
We can assign n-bit values to sub-buses, for any n
We can create n-bit bus pins, for any n
Another example of assigning a multi-bit value to a sub-bus
Relevant bus tips

## Slide 69
/* 16-bit adder */
CHIP Add16 {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
CHIP Foo {
IN x[8], y[8], z[16]
OUT out[16]
PARTS
...
Add16 (a[0..7] = x, a[8..15] = y, b = z, out = …);
...
Add16 (a = …, b = …, out[0..3] = t1, out[4..15] = t2);
...
}
Creating an n-bit bus (internal pin)
Sub-bussing:
We can assign n-bit values to sub-buses, for any n
We can create n-bit bus pins, for any n
Another example of assigning a multi-bit value to a sub-bus
Relevant bus tips

## Slide 70: Perspective
Combinational logic
Our adder design is very basic: no parallelism
It pays to optimize adders
Our ALU is also very basic: no multiplication, no division
Where is the seat of more advanced math operations? a typical hardware/software tradeoff.