## Slide 1: Sequential Logic
Introduction to Computer
Yung-Yu Chuang
with slides by Sedgewick & Wayne (introcs.cs.princeton.edu), Nisan & Schocken (www.nand2tetris.org) and Harris & Harris (DDCA)

## Slide 2: Logic gates
Model: And, Or, Not, …
Simple, and powerful:
Logic gates can realize any Boolean function, and can be combined to form powerful chips, like an ALU
But, as a general model of computation, logic gates fall short
Limitations
Logic gates cannot store information (bits) over time
Feedback loops are not allowed: A chip’s output cannot serve as its input
Logic gates can handle only inputs of a fixed size. For example, we can build an Or3 gate, and an Or4 gate, and so on, but we cannot build a single gate that computes Or for any given number of inputs
Extension
Allow logic gates to be sensitive to the progression of time.
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 3: Time-independent Logic
So far we ignored time
The chip’s inputs were just “sitting there” – fixed and unchanging
The chip’s output was a function (“combination”) of the current inputs, and the current inputs only
This style of gate logic is sometimes called:
  time-independent logic
  combinational logic
All the chips that we discussed and developed so far were combinational
ALU
+
0101
1000
1101
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 4: Combinational vs. Sequential Circuits
Combinational circuits.
  Output determined solely by inputs.
  Can draw with no loops.
  Ex: majority, adder, ALU.
Sequential circuits.
  Output determined by inputs and previous outputs.
  Ex: memory, program counter, CPU.

## Slide 5: Combinational vs. Sequential Circuits
Combinational circuits.
  Basic abstraction = switch.
  In principle, can build TOY computer with a combinational circuit.
    255  16 = 4,080 inputs  24080 rows in truth table!
    no simple pattern
    each circuit element used at most once
Sequential circuits. Reuse circuit elements by storing bits in "memory."
ALU
combinational
Memory
state
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 6: Time
Software needs:
x = 17
Example (variables):
for i in range(0, 10):
print(i)
Example (iteration):
The hardware must handle the physical time delays associated with computing and moving data from one chip to another.
Hardware needs:
The hardware must be able to remember things, over time:
The hardware must be able to do things, one at a time (sequentially):
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 7: Representing time
physical time:
Arrow of time:
Continuous
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 8: Representing time
1
0
clock:
physical time:
Arrow of time:
Continuous
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 9: Chip behavior over time (example: Not gate)
1
0
clock:
time: 1 2 3 4 5 . . .
physical time:
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 10: Chip behavior over time (example: Not gate)
1
0
clock:
time: 1 2 3 4 5 . . .
physical time:
(example)
in:
0
1
0
1
out:
(Not(in))
Arrow of time:
Continuous
in:
(arbitrary values)
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 11: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
in:
(arbitrary values)
(example)
out:
(Not(in))
Desired / idealized behavior of the in and out signals:
That’s how we want the hardware to behave
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 12: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
(example)
Arrow of time:
Continuous
out:
(Not(in))
in:
(arbitrary values)
Actual behavior of the in and out signals:
Influenced by physical time delays
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 13: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
(example)
Time delays
Propagation delays
Computation delays
out:
(Not(in))
in:
(arbitrary values)
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another
Cycle length
Design parameter
Set to be slightly > max(time delays)
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 14: Chip behavior over time (example: Not gate)
1
0
0
1
clock:
time: 1 2 3 4 5 . . .
0
1
physical time:
Resulting effect:
Combinational chips react “immediately” to their inputs
Facilitated by the decision to track changes only at cycle ends
out:
(Not(in))
(example)
in:
(arbitrary values)
Arrow of time:
Continuous
Discrete time:
Design decision: Track state changes only when advancing from one time-step to another
Notes: The same principle as we design adder
We can only compute functions which can be described by rules (computable). For the functions which can not be described compactly, they are not computable.

## Slide 15: Clock
Clock.
  Fundamental abstraction: regular on-off pulse.
    on: fetch phase
    off: execute phase
  External analog device.
  Synchronizes operations of different circuit elements.
  Requirement: clock cycle longer than max switching time.
cycle time
Clock
on
off
Notes: Clock is outside Boolean/digital logic framework. Need external source. Can wire up minute hand of Big Ben to computer. In real
computer, clock abstraction implemented using electric phenomenon like a crystal oscillator, a piezoelectric device that generates oscillating voltage
Clock is like a conductor's baton or metrononme (asssuming no ritardando = ree-tar-DAHN-doe), except that it beats at rate of millions of times per second. Note 1GHz machine cycle takes 1 billionth of a second (nanosecond). To put things in perspective, a standard light bulb switches on and off at the rate of 120 times per second! (Patt, Patel, p. 83) In that time, a computer completes around 10 million machine cycles.
Computer engineers make circuit, then crank up the clock as fast as possible until circuit no longer works. Then crank it down just a bit, and sell it. Maybe manufactures should put dial on the computer and let user crank it up until their program no longer works! To get faster computer, need to adjust wire lengths, circuit layout, change components.

## Slide 16: How much does it Hert?
Frequency is inverse of cycle time.
  Frequency of 1 Hz (Hertz) means that there is 1 cycle per second.
    1 kilohertz (kHz) means 1000 cycles/sec.
    1 megahertz (MHz) means 1 million cycles/sec.
    1 gigahertz (GHz) means 1 billion cycles/sec.
    1 terahertz (THz) means 1 trillion cycles/sec.
Heinrich Rudolf Hertz (1857-1894)
Physical clock
An oscillator is used to deliver an ongoing train of “tick/tock” signals
“1 MHz electronic oscillator circuit which uses the resonant properties of an internal quartz crystal to control the frequency. Provides the clock signal for digital devices such as computers.” (Wikipedia)
Notes: unit named in honor of Heinrich Rudolf Hertz.
BTW, no such thing as 1 "hert". This comes as a surprise to a recent graduate of my department, now a PhD candidate at Stanford
THz clock: to compare, it would take an average person more than 15,000 years to turn a light switch on and off a trillion times.

## Slide 17: Flip-Flop
Flip-flop
  A small and useful sequential circuit
  Abstraction that remembers one bit
  Basis of important computer components for
    register
    memory
    counter
  There are several flavors

## Slide 18: S-R flip flop
Q=S+RQ
R | S | Q
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 19: S-R flip flop
Q=S+RQ
R | S | Q
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 20: Relay-based flip-flop
  Ex. Simplest feedback loop.
  Two relays A and B, both connected to power, each blocked by the other.
  State determined by whichever switches first. The state is latched.
  Stable.
input1
output1
input2
output2

## Slide 21: SR Flip Flop
SR flip flop. Two cross-coupled NOR gates.
Q=R(S+Q)
R | S | Q
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
R
S
Q

## Slide 22: Flip-Flop
Flip-flop.
  A way to control the feedback loop.
  Abstraction that "remembers" one bit.
  Basic building block for memory and registers.
Caveat. Need to deal with switching delay.
Notes: RS flip-flop

## Slide 23: Truth Table and Timing Diagram
Truth table.
  Values vary over time.
  S(t), R(t), Q(t) denote value at time t.
Sample timing diagram for SR flip-flop.
Q(t+)
SR Flip Flop Truth Table
S(t)
0
0
1
0
0
0
0
0
R(t)
0
0
1
1
Q(t)
0
1
0
1
1
1
1
1
1
1
0
0
1
1
0
1
0
1
Q
R
S
time
1
0
1
0
1
0
e
e
Notes: Can break down truth table into 4 regions (remember, reset, set, excluded for technical reasons)
Need to introduce time into equation with sequential circuits.
Note Q(t+e) becomes input at next time quantum.
epsilon exaggerated for effect – it is very small relative to other signals: we'll ignore timing delays in future slides.

## Slide 24: Clock
Clock.
  Fundamental abstraction: regular on-off pulse.
    on: fetch phase
    off: execute phase
  External analog device.
  Synchronizes operations of different circuit elements.
  Requirement: clock cycle longer than max switching time.
cycle time
Clock
on
off
Notes: Clock is outside Boolean/digital logic framework. Need external source. Can wire up minute hand of Big Ben to computer. In real
computer, clock abstraction implemented using electric phenomenon like a crystal oscillator, a piezoelectric device that generates oscillating voltage
Clock is like a conductor's baton or metrononme (asssuming no ritardando = ree-tar-DAHN-doe), except that it beats at rate of millions of times per second. Note 1GHz machine cycle takes 1 billionth of a second (nanosecond). To put things in perspective, a standard light bulb switches on and off at the rate of 120 times per second! (Patt, Patel, p. 83) In that time, a computer completes around 10 million machine cycles.
Computer engineers make circuit, then crank up the clock as fast as possible until circuit no longer works. Then crank it down just a bit, and sell it. Maybe manufactures should put dial on the computer and let user crank it up until their program no longer works! To get faster computer, need to adjust wire lengths, circuit layout, change components.

## Slide 25: Clocked S-R flip-flop

## Slide 26: Clocked D flip-flop

## Slide 27: Stand-Alone Register

## Slide 28: Register file interface

## Slide 29: Register file implementation

## Slide 30: Multiplexer
When s=0, return x; otherwise, return y.
Example: (Y  S)  (X  S)
Two-input multiplexer

## Slide 31: 4-to-1 multiplexer
4MUX
x0
x1
x2
x3
z
s0
s1

## Slide 32: 4-to-1 multiplexer
4MUX
x0
x1
x2
x3
z
s0
s1
2MUX
2MUX
2MUX
x0
x1
x2
x3
z
s0
s1

## Slide 33: 8-to-1 Multiplexer
2N-to-1 multiplexer
  N select inputs, 2N data
  inputs, 1 output
  Copies “selected” data input
  bit to output

## Slide 34: 8-to-1 Multiplexer
2N-to-1 multiplexer
  N select inputs, 2N data
  inputs, 1 output
  Copies “selected” data input
  bit to output

## Slide 35: 4-Wide 2-to-1 Multiplexer
Goal: select from one of two 4-bit buses

## Slide 36: 4-Wide 2-to-1 Multiplexer
Goal: select from one of two 4-bit buses
  Implemented by layering 4 2-to-1 multiplexer

## Slide 37: k-Wide n-to-1 Multiplexer
Goal: select from one of n k-bit buses
  Implemented by layering k n-to-1 multiplexer

## Slide 38: Register file implementation

## Slide 39: Memory Overview
Computers and TOY have several memory components.
  Program counter.
  Registers.
  Main memory.
Implementation. Use one flip-flop for each bit of memory.
Access. Memory components have different access mechanisms.
Organization. Need mechanism to manipulate groups of related bits.
TOY has 16 bit words, 8 bit memory addresses, and 4 bit register names.
Notes: memory is abstraction: we use flip-flops
  TOY has 16-bit words.
  Memory hierarchy makes architecture manageable.
It wasn't always this way. First computer memory implemented with vacuum tubes. Big advance in 1960's was "core memory." Used magnetism. Human still had to wire each bit individually. Nowadays, this is done my machine and cost/bit has decreased dramatically.

## Slide 40: Register Bit
Register bit. Extend a flip-flop to allow easy access to values.

## Slide 41: Register Bit
Register bit. Extend a flip-flop to allow easy access to values.
DW
DW
D
W

## Slide 42: Memory Bit: Interface
Memory bit. Extend a flip-flop to allow easy access to values.
[ TOY PC, IR ]
[ TOY main memory ]
[ TOY registers ]

## Slide 43: Memory Bit: Switch Level Implementation
Memory bit. Extend a flip-flop to allow easy access to values.
[ TOY PC, IR ]
[ TOY main memory ]
[ TOY registers ]
Notes: redownload figures from book when Bob fixes (there is a ppt hack in the last two)

## Slide 44: Processor Register
Processor register.
  Stores k bits.
  Register contents always available on output bus.
  If enable write is asserted, k input bits get copied into register.
Ex 1. TOY program counter (PC) holds 8-bit address.
Ex 2. TOY instruction register (IR) holds 16-bit current instruction.

## Slide 45: Processor Register
Processor register.
  Stores k bits.
  Register contents always available on output bus.
  If enable write is asserted, k input bits get copied into register.
Ex 1. TOY program counter (PC) holds 8-bit address.
Ex 2. TOY instruction register (IR) holds 16-bit current instruction.

## Slide 46: Processor Register
Processor register.
  Stores k bits.
  Register contents always available on output bus.
  If enable write is asserted, k input bits get copied into register.
Ex 1. TOY program counter (PC) holds 8-bit address.
Ex 2. TOY instruction register (IR) holds 16-bit current instruction.

## Slide 47: Memory Bank
Memory bank.
  Bank of n registers; each stores k bits.
  Read and write information to one of n registers.
  Address inputs specify which one.
  Addressed bits always appear on output.
  If write enabled, k input bits are copied into addressed register.
Ex 1. TOY main memory.
  256-by-16 memory bank.
Ex 2. TOY registers.
  16-by-16 memory bank.
  Two output buses.
(four 6-bit words)
log2n address bits needed
2-bit address
6-bit input bus
6-bit output bus

## Slide 48: Memory: Interface
(four 6-bit words)

## Slide 49: Memory: Component Level Implementation

## Slide 50: Memory: Switch Level Implementation
(four 6-bit words)

## Slide 51: TOY sequential circuits
Sequential circuits add "state" to digital hardware.
  Flip-flop. [represents 1 bit]
  TOY word. [16 flip-flops]
  TOY registers. [16 words]
  TOY main memory. [256 words]
Modern technologies for registers and main memory are different.
  Few registers, easily accessible, high cost per bit.
  Huge main memories, less accessible, low cost per bit.
  Drastic evolution of technology over time.
Next. Build a complete TOY computer.

## Slide 52: Project 3
www.nand2tetris.org
All the necessary project 3 files are available in:
nand2tetris / projects / 03

## Slide 53: Project 3
Given:
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
Build:
Bit
Register
PC
RAM8
RAM64
RAM512
RAM4K
RAM16K

## Slide 54: Registers
Designed to:
“Store” / “remember” / “maintain” / “persist” a value , until...
“Instructed” to “load”, and then “store”, another value.
out
in
load
Bit
1-bit register
Register
in
w
out
w
load
multi-bit register
x = 17, 17, 17, 17, 17, 17, 17, ..., 17
x = 21, 21, 21, 21, 21, 21, ..., 21
time:
loading
maintaining state
loading
maintaining state

## Slide 55: Memory hierarchy
1-bit
register
Bit
Data
Flip-Flop
DFF
0
1
n-1
...
Register
Random Access Memory
RAMn
Register
Register
16-bit register
...
Register
Bit
Bit
Bit
?
DFF

## Slide 56: DFF
examples of arbitrary inputs
1
2
3
4
5
6
7
8
time:
0
1
1
0
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 57: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 58: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 59: DFF
1
2
3
4
5
6
7
8
0
1
1
0
time:
examples of arbitrary inputs
in:
out:
out(t) = in(t – 1)
out
in
DFF
Data Flip Flop (aka latch)
The most elementary sequential gate: Outputs the input in the previous time-step

## Slide 60: 1-bit register
out
in
load
Bit
/** 1-bit register:
if load(t – 1) then out(t) = in(t – 1)
else out(t) = out(t – 1)) */
CHIP Bit {
IN in, load;
OUT out;
PARTS:
// Put your code here:
}
Bit.hdl
in
load
out
Implementation tip:
Follow the chip diagram

## Slide 61: 16-bit register
Register.hdl
Register
in
16
out
16
load
/** 1-bit register:
if load(t – 1) then out(t) = in(t – 1)
else out(t) = out(t – 1)) */
CHIP Bit {
IN in[16], load;
OUT out[16];
PARTS:
// Put your code here:
}
16
out
load
16
in
...
Implementation tip:
Follow the chip diagram
Partial diagram, showing some of the chip-parts, without connections

## Slide 62: Counter
Later in the course, we will see that the computer must keep track of which instruction should be fetched and executed next
This task is regulated by a register typically called Program Counter
We’ll use the PC to store the address of the instruction that should be fetched and executed next
The PC should support three abstractions:
  Reset: fetch the first instruction
  Next: fetch the next instruction
  Goto: fetch instruction n
PC = 0
PC++
PC = n

## Slide 63: Counter
if reset(t) out(t + 1) = 0
else if load(t) out(t + 1) = in(t)
else if inc(t) out(t + 1) = out(t) + 1
else out(t + 1) = out(t)
PC (counter)
in
16
out
16
load
inc
reset

## Slide 64: Counter
if reset(t) out(t + 1) = 0
else if load(t) out(t + 1) = in(t)
else if inc(t) out(t + 1) = out(t) + 1
else out(t + 1) = out(t)
PC (counter)
in
16
out
16
load
inc
reset
To read:
probe out
To reset:
assert reset,
set the other control bits to 0
To count:
assert inc,
set the other control bits to 0
To set:
set in to v,
assert load,
set the other control bits to 0
Usage:

## Slide 65: 16-bit counter
Implementation tip: Can be built from a Register, an Incrementer, and Mux’s
/**
A 16-bit counter with control bits.
if reset(t – 1) out(t) = 0 // resetting
else if load(t – 1) out(t) = in(t – 1) // setting
else if inc(t – 1) out(t) = out(t – 1) + 1 // incrementing
else out(t) = out(t – 1) // maintaining
*/
CHIP PC {
IN in[16], load, inc, reset;
OUT out[16];
PARTS:
// Put your code here:
}
PC (counter)
in
16
out
16
load
inc
reset

## Slide 66: Project 3
Given:
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
Build the following chips
Bit
Register
PC
RAM8
RAM64
RAM512
RAM4K
RAM16K

## Slide 67: 8-register RAM: abstraction
/*
Let M stand for the state of the register
selected by address.
if load(t – 1) then {M = in(t), out(t) = M}
else out(t) = M
*/
CHIP RAM8 {
IN in[16], load, address[3];
OUT out[16];
PARTS:
// Put your code here:
}
RAM8.hdl
out
in
load
Register
...
RAMn
Register
Register
address
3
16
16

## Slide 68: 8-register RAM: implementation
DMux
(1 to 8)
Register
in
16
load
out
Register
in
load
out
Register
in
load
out
...
Mux
(8 to 1)
out
16
in
16
address
3
load
Partial diagram, showing some of the chip-parts, without connections
16
16
16
16
16
Implementation tip:
Follow the chip diagram

## Slide 69: Project 3
Given:
All the chips built in projects 1 and 2
Data Flip-Flop (built-in DFF gate)
A family of RAM chips
Build the following chips
Bit
Register
PC
RAM8
RAM64
RAM512
RAM4K
RAM16K

## Slide 70: N-Register RAM
out
in
load
16
Register
...
RAMn
Register
Register
address
k
16
/*
Let M stand for the state of the register
selected by address.
if load(t – 1) then {M = in(t), out(t) = M}
else out(t) = M
*/
CHIP RAMn {
IN in[16], load, address[k];
OUT out[16];
PARTS:
// Put your code here:
}
RAMn.hdl

## Slide 71: N-Register RAM
chip name | n | k
RAM8 | 8 | 3
RAM64 | 64 | 6
RAM512 | 512 | 9
RAM4K | 4096 | 12
RAM16K | 16384 | 14
out
in
load
16
Register
...
RAMn
Register
Register
address
k
16
Implementation tips
Think about the RAM’s address input as consisting of two fields:
  One field selects a RAM-part;
  The other field selects a register within that RAM-part
Use logic gates to effect this addressing scheme.