## Slide 1: Computer Architecture
www.nand2tetris.org
Building a Modern Computer From First Principles
Notes: 1

## Slide 2: Where we are at:
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12

## Slide 3: The Hack computer
A 16-bit machine consisting of the following elements:
The program is stored in a ROM.

## Slide 4: The A-instruction
@value
value is a non-negative decimal number <= 215-1 or
A symbol referring to such a constant
0value
value is a 15-bit binary number
symbolic
binary
@21
0000 0000 0001 0101
Example

## Slide 5: The C-instruction
dest = comp ; jump
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
symbolic
binary
opcode
]
not used
comp
dest
jump

## Slide 6: The C-instruction
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
comp
dest
jump

## Slide 7: The C-instruction
A D M
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
comp
dest
jump
dest | d | d | d | effect: the value is stored in:
null | 0 | 0 | 0 | the value is not stored
M | 0 | 0 | 1 | RAM[A]
D | 0 | 1 | 0 | D register
DM | 0 | 1 | 1 | D register and RAM[A]
A | 1 | 0 | 0 | A register
AM | 1 | 0 | 1 | A register and RAM[A]
AD | 1 | 1 | 0 | A register and D register
ADM | 1 | 1 | 1 | A register, D register, and RAM[A]

## Slide 8: The C-instruction
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
comp
dest
jump
jump | j | j | j | effect:
null | 0 | 0 | 0 | no jump
JGT | 0 | 0 | 1 | if comp > 0 jump
JEQ | 0 | 1 | 0 | if comp = 0 jump
JGE | 0 | 1 | 1 | if comp ≥ 0 jump
JLT | 1 | 0 | 0 | if comp < 0 jump
JNE | 1 | 0 | 1 | if comp ≠ 0 jump
JLE | 1 | 1 | 0 | if comp ≤ 0 jump
JMP | 1 | 1 | 1 | Unconditional jump
< = >

## Slide 9
assembly code v.s. machine code
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
0000000000000001
1110001100001000
0000000000010110
1110101010000111
Target code
assemble
Hack assembly/machine language
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)
Hack assembler
or CPU emulator

## Slide 10: The Hack computer
Main parts of the Hack computer:
Instruction memory (ROM)
Memory (RAM):
  Data memory
  Screen (memory map)
  Keyboard (memory map)
CPU
Computer (the logic that holds everything together).
A 16-bit stored program platform
The instruction memory and the data memory are physically separate
Screen: 512 rows by 256 columns, black and white
Keyboard: standard
Designed to execute programs written in the Hack machine language
Can be easily built from the chip-set that we built so far in the course

## Slide 11: Multiplexer
Goal: select from one of n k-bit buses
  Implemented by layering k n-to-1 multiplexer

## Slide 12: Hack ALU
out(x, y, control bits) =
x+y, x-y, y–x,
0, 1, -1,
x, y, -x, -y,
x!, y!,
x+1, y+1, x-1, y-1,
x&y, x|y

## Slide 13: Hack ALU

## Slide 14: Registers

## Slide 15: ROM (Instruction memory)
Function:
The ROM is pre-loaded with a program written in the Hack machine language
The ROM chip always emits a 16-bit number: out = ROM32K[address]
This number is interpreted as the current instruction.

## Slide 16: RAM (data memory)
We will discuss the details for Hack’s data memory later.
32K x 16
RAM
W
Din
addr
Dout
16
16
15

## Slide 17: Clock
Clock.
  Fundamental abstraction: regular on-off pulse.
    on: fetch phase
    off: execute phase
  External analog device.
  Synchronizes operations of different circuit elements.
  Requirement: clock cycle longer than max switching time.
cycle time
Clock
on
off
Notes: Clock is outside Boolean/digital logic framework. Need external source. Can wire up minute hand of Big Ben to computer. In real
computer, clock abstraction implemented using electric phenomenon like a crystal oscillator, a piezoelectric device that generates oscillating voltage
Clock is like a conductor's baton or metrononme (asssuming no ritardando = ree-tar-DAHN-doe), except that it beats at rate of millions of times per second. Note 1GHz machine cycle takes 1 billionth of a second (nanosecond). To put things in perspective, a standard light bulb switches on and off at the rate of 120 times per second! (Patt, Patel, p. 83) In that time, a computer completes around 10 million machine cycles.
Computer engineers make circuit, then crank up the clock as fast as possible until circuit no longer works. Then crank it down just a bit, and sell it. Maybe manufactures should put dial on the computer and let user crank it up until their program no longer works! To get faster computer, need to adjust wire lengths, circuit layout, change components.

## Slide 18: Design a processor
How to build a processor (Hack, this time)
  Develop instruction set architecture (ISA)
    16-bit words, two types of machine instructions
  Determine major components
    ALU, registers, program counter, memory
  Determine datapath requirements
    Flow of bits
  Analyze how to implement each instruction
    Determine settings of control signals

## Slide 19: Hack programming reference card
Hack commands:
A-command: @value // A<-value; M=RAM[A]
C-command: dest = comp ; jump // dest = and ;jump // are optional
Where:
comp =
0 , 1 , -1 , D , A , !D , !A , -D , -A , D+1 , A+1 , D-1, A-1 , D+A , D-A , A-D , D&A , D|A,
M , !M , -M , M+1, M-1 , D+M, D-M, M-D, D&M, D|M
dest = M, D, A, MD, AM, AD, AMD, or null
jump = JGT , JEQ , JGE , JLT , JNE , JLE , JMP, or null
In the command dest = comp; jump, the jump materialzes (PC<-A) if (comp jump 0) is true. For example, in D=D+1,JLT, we jump if D+1 < 0.

## Slide 20: Fetch and execute
  In Toy, we have two phases: fetch and execution .
  We use two cycles since fetch and execute phases each access memory and alter program counter.
20
Fetch
Clock
Execute
Fetch
Phase 1
fetch
Phase 3
execute
Phase 2
fetch & clock
Phase 4
execute & clock
    fetch [set memory address from pc]
    fetch and clock [write instruction to IR]
    execute [set ALU inputs from registers]
    execute and clock [write result of ALU to registers]

## Slide 21: Toy architecture
PC
Registers
W
W Data
A Data
B Data
W Addr
A Addr
B Addr
+
1
Memory
W
W Data
Addr
R Data
IR
op
d
s
t
Cond
Eval
A
L
U
2
5
1
0
1
0
0
1
1
0
10
01
00
  Both fetch and execute would access memory. To avoid conflict, we add a MUX. Similar for PC.
  In addition, we need a register IR to store the instruction.

## Slide 22: Fetch and execute
  In Hack, we avoid two cycles and IR by using two separate memory chips, one for data and the other for instruction.
22

## Slide 23: Design a processor
How to build a processor (Hack, this time)
  Develop instruction set architecture (ISA)
    16-bit words, two types of machine instructions
  Determine major components
    ALU, registers, program counter, memory
  Determine datapath requirements
    Flow of bits
  Analyze how to implement each instruction
    Determine settings of control signals

## Slide 24: Program counter
Program counter emits the address of the next instruction.
  To start/restart the program execution: PC=0
  No jump: PC++
  Unconditional jump: PC=A
  Conditional jump: if (cond.) PC=A else PC++
Program counter
(PC)
reset
W
Din
Dout
15
15
Note that the design is slightly different from your project #3.

## Slide 25: Program counter
if (reset) PC=0
else if (W) PC=Din
else PC++

## Slide 26: Program counter
if (reset) PC=0
else if (W) PC=Din
else PC++
0
1
15-bit register
W
+
1
0
1
0
reset
W
Din
Dout

## Slide 27: Hack architecture (component)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
x
y
zr
ng
CPU
reset
Clock

## Slide 28: Design a processor
How to build a processor (Hack, this time)
  Develop instruction set architecture (ISA)
    16-bit words, two types of machine instructions
  Determine major components
    ALU, registers, program counter, memory
  Determine datapath requirements
    Flow of bits
  Analyze how to implement each instruction
    Determine settings of control signals

## Slide 29: Hack architecture (data path)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
x
y
zr
ng
CPU
reset
Fetch: instruction=ROM[PC]
@value // A<-value; M=RAM[A]
[ADM] = x op y; jump // x=D; y=A or M; if jump then PC<-A

## Slide 30: Hack architecture (data path)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
Fetch: instruction=ROM[PC]
@value // A<-value; M=RAM[A]
[ADM] = x op y; jump // x=D; y=A or M; if jump then PC<-A

## Slide 31: Design a processor
How to build a processor (Hack, this time)
  Develop instruction set architecture (ISA)
    16-bit words, two types of machine instructions
  Determine major components
    ALU, registers, program counter, memory
  Determine datapath requirements
    Flow of bits
  Analyze how to implement each instruction
    Determine settings of control signals

## Slide 32: Hack architecture (data path)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset

## Slide 33: Hack architecture (control)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
MUX_A
W_A
MUX_ALU
OP_ALU
6
W_PC
writeM
R_PC
W_D
A total of 13 control signals

## Slide 34: Hack architecture (control)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
MUX_A
W_A
MUX_ALU
OP_ALU
6
W_PC
writeM
R_PC
W_D
control

## Slide 35: Hack architecture (control)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
MUX_A
W_A
MUX_ALU
OP_ALU
6
W_PC
writeM
R_PC
W_D
control

## Slide 36: Hack architecture (control)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
6
control

## Slide 37: Hack architecture (control)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
6
control
reset

## Slide 38: Hack architecture (control)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
MUX_A
W_A
MUX_ALU
OP_ALU
6
W_PC
writeM
R_PC
W_D
control
reset
zr
ng
instruction

## Slide 39: Hack architecture (control)
Inputs: instruction, zr, ng
  instruction
Outputs:
  OP_ALU = C1C2C3C4C5C6
  MUX_A =
  MUX_ALU = A
  W_A = ( & D1) +
  W_D = & D2
  writeM = & D3
  W_PC = & ( (J1&ng) + (J2&zr) + (J3&gt) ); gt = ng & zr
111A C1C2C3C4 C5C6 D1D2 D3J1J2J3
0 value
I
15
I
14..0
I
15
I
15
I
15
I
15
I
15
I
15

## Slide 40: Hack architecture (trace @10 / D=M+1;JGE )
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
W
0
1
0
1
x
y
zr
ng
CPU
reset
MUX_A
W_A
MUX_ALU
OP_ALU
6
W_PC
writeM
R_PC
W_D
control
reset
zr
ng
instruction

## Slide 41: Hack architecture (CPU interface)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
control
W
0
1
0
1
x
y
zr
ng
CPU
instruction
inM
reset
outM
writeM
PC
addressM
reset
zr
ng

## Slide 42: Hack architecture (CPU interface)
A
L
U
PC
RAM
W
Din
addr
Dout
ROM
addr
Dout
A
W
D
W
control
W
0
1
0
1
x
y
zr
ng
inM
reset
writeM
PC
addressM
reset
zr
ng
outM
instruction
CPU

## Slide 43: Hack CPU

## Slide 44
Control (focus on the yellow chips only)
ALU
Mux
D
A/M
a-bit
D register
A register
A
M
RAM
(selected register)
ROM
(selected register)
PC
Instruction
In the Hack architecture:
ROM = instruction memory
Program = sequence of 16-bit numbers, starting at ROM[0]
Current instruction = ROM[PC]
To select instruction n from the ROM, we set A to n, using the instruction @n
address input
address input

## Slide 45
Side note (focus on the yellow chip parts only)
ALU
Mux
D
A/M
a-bit
D register
A register
A
M
RAM
(selected register)
ROM
(selected register)
PC
Instruction
address input
address input
In the Hack architecture, the A register could address both the RAM and the ROM, simultaneously. Therefore:
Command pairs like @addr followed by D=M;someJumpDirective make no sense
Best practice: in well-written Hack programs, a C-instruction should contain
  either a reference to M, or
  a jump directive,
but not both.
Notes: 45

## Slide 46: The Hack computer (put together)
A 16-bit machine consisting of the following elements:
Both memory chips are 16-bit wide and have 15-bit address space.

## Slide 47: RAM (data memory)
The RAM used in Hack is different from a normal RAM. It also plays the role for I/O.
Programmers usually use high-level library for I/O, such as printf, drawline.
But, at low-level, we usually need to manipulate bits directly for I/O.
RAM
W
Din
addr
Dout
16
16
15

## Slide 48: Displays
CRT displays
  resolution
  refresh rate

## Slide 49: keyboard

## Slide 50: Memory: conceptual / programmer’s view
Using the memory:
To record or recall values (e.g. variables, objects, arrays), use the first 16K words of the memory
To write to the screen (or read the screen), use the next 8K words of the memory
To read which key is currently pressed, use the next word of the memory.
Data
Screen memory map
Keyboard map
Memory
Keyboard
Screen
Notes: 50

## Slide 51: Memory: physical implementation
Access logic:
Access to any address from 0 to 16,383 results in accessing the RAM16K chip-part
Access to any address from 16,384 to 24,575 results in accessing the Screen chip-part
Access to address 24,576 results in accessing the keyboard chip-part
Access to any other address is invalid.
load
out
in
16
15
16
RAM16K
(16K mem. chip)
address
0
16383
Screen
(8K mem. chip)
16384
24575
24576
Keyboard
(one register)
Memory
Keyboard
Screen
The Memory chip is essentially a package that integrates the three chip-parts RAM16K, Screen, and Keyboard into a single, contiguous address space.
This packaging effects the programmer’s view of the memory, as well as the necessary I/O side-effects.
Notes: 51

## Slide 52: Data memory
Low-level (hardware) read/write logic:
To read RAM[k]: set address to k, probe out
To write RAM[k]=x: set address to k, set in to x, set load to 1, run the clock
High-level (OS) read/write logic:
To read RAM[k]: use the OS command out = peek(k)
To write RAM[k]=x: use the OS command poke(k,x)
peek and poke are OS commands whose implementation should effect the same behavior as the low-level commands
More about peek and poke this later in the course, when we’ll write the OS.
load

## Slide 53: Screen
In the Hack platform, the screen is implemented as an 8K 16-bit RAM chip with a side effect of refreshing.
The Screen chip has a basic RAM chip functionality:
  read logic: out = Screen[address]
  write logic: if load then Screen[address] = in
Side effect:
Continuously refreshes a 256 by 512 black-and-white screen device
The bit contents of the Screen chip is called the “screen memory map”
The simulated 256 by 512 B&W screen
  When loaded into the hardware simulator, the built-in Screen.hdl chip opens up a screen window; the simulator then refreshes this window from the screen memory map several times each second.
Simulated screen:
Notes: Use the hardware simulator to demo memory chip

## Slide 54
(16384)
To set pixel (row,col) black
word=Screen[32*row + col/16]
(RAM[16384 + 32*row + col/16])
Set the (col%16)-th bit of word to 1
Commit word to the RAM
(High-level: use the OS command drawPixel(row,col))
Screen memory map
refresh
Notes: 1d linear array to 2d array mapping. Test real example, eg. (3, 60)

## Slide 55: keyboard
A 16-bit register is used to keep the key stroke.
When a key is pressed on the keyboard, the key’s scan code appears in the keyboard memory map .

## Slide 56: keyboard
A 16-bit register is used to keep the key stroke.
When a key is pressed on the keyboard, the key’s scan code appears in the keyboard memory map .

## Slide 57: Keyboard
Keyboard chip: a single 16-bit register
Input: scan-code (16-bit value) of the currently pressed key, or 0 if no key is pressed
Output: same
How to read the keyboard:
Low-level (hardware): probe the contents of the Keyboard chip
High-level: use the OS command keyPressed()
(effects the same operation, discussed later in the course, when we’ll write the OS).
Special keys:
The keyboard is implemented as a built-in Keyboard.hdl chip. When this java chip is loaded into the simulator, it connects to the regular keyboard and pipes the scan-code of the currently pressed key to the keyboard memory map.
The simulated keyboard enabler button
Simulated keyboard:
Notes: Demo with Hardware simulator

## Slide 58: Some scan codes
key | code
(space) | 32
! | 33
“ | 34
# | 35
$ | 36
% | 37
& | 38
‘ | 39
( | 40
) | 41
* | 42
+ | 43
, | 44
- | 45
. | 46
/ | 47
key | code
0 | 48
1 | 49
… | …
9 | 57
: | 58
; | 59
< | 60
= | 61
> | 62
? | 63
@ | 64
key | code
A | 65
B | 66
C | …
… | …
Z | 90
[ | 91
/ | 92
] | 93
^ | 94
_ | 95
` | 96
key | code
a | 97
b | 98
c | 99
… | …
z | 122
key | code
newline | 128
backspace | 129
left arrow | 130
up arrow | 131
right arrow | 132
down arrow | 133
home | 134
end | 135
Page up | 136
Page down | 137
insert | 138
delete | 139
esc | 140
f1 | 141
. . . | . . .
f12 | 152
{ | 123
¦ | 124
} | 125
~ | 126
(Subset of Unicode)

## Slide 59: Keyboard memory map
To check which key is currently pressed:
  Probe the content of the Keyboard chip
  In the Hack computer, probe the content of RAM[24576]
  If the register contains 0, no key is pressed.

## Slide 60: The Hack computer (put together)
A 16-bit machine consisting of the following elements:
Both memory chips are 16-bit wide and have 15-bit address space.
Screen
Keyboard

## Slide 61: Assembly programming with I/O
Hack language convention:
SCREEN: base address of the screen memory map, 16,384.
KBD: address of the keyboard memory map, 24,576.

## Slide 62: Example: draw a rectangle
Draw a filled rectangle at the upper left corner of the screen, 16 pixels wide and RAM[0] pixels long. (demo)
16 pixels wide
RAM[0] pixels long

## Slide 63: Example: draw a rectangle (pseudo code)
// for (i=0; i<n; i++)
// draw 16 black pixels at the beginning of row i
addr = SCREEN
n = RAM[0]
i = 0
LOOP:
if (i>=n) goto END
RAM[addr] = -1 // 1111 1111 1111 1111
addr = addr+32 // advances to the next row
i++;
goto LOOP
END:
goto END

## Slide 64: Example: draw a rectangle (assembly)
addr = SCREEN
n = RAM[0]
i = 0
LOOP:
if (i>=n) goto END
RAM[addr] = -1
addr = addr+32
i++;
goto LOOP
END:
goto END
  @SCREEN
  D=A
  @addr
  M=D // addr = SCREEN
  @0
  D=M
  @n
  M=D // n = RAM[0]
  @i
  M=0 // i=0

## Slide 65: Example: draw a rectangle (assembly)
addr = SCREEN
n = RAM[0]
i = 0
LOOP:
if (i>=n) goto END
RAM[addr] = -1
addr = addr+32
i++;
goto LOOP
END:
goto END
  (LOOP)
  @i
  D=M
  @n
  D=D-M
  @END
  D; JGE
  @addr
  A=M
  M=-1

## Slide 66: Example: draw a rectangle (assembly)
addr = SCREEN
n = RAM[0]
i = 0
LOOP:
if (i>=n) goto END
RAM[addr] = -1
addr = addr+32
i++;
goto LOOP
END:
goto END
  (LOOP)
  @i
  D=M
  @n
  D=D-M
  @END
  D; JGE
  @addr
  A=M
  M=-1

## Slide 67: Example: draw a rectangle (assembly)
addr = SCREEN
n = RAM[0]
i = 0
LOOP:
if (i>=n) goto END
RAM[addr] = -1
addr = addr+32
i++;
goto LOOP
END:
goto END
  @32
  D=A
  @addr
  M=D+M // addr = addr+32
  @i
  M=M+1 // i++
  @LOOP
  0; JMP // goto LOOP
  (END)
  @END
  0; JMP

## Slide 68: Example: draw a rectangle (assembly)
addr = SCREEN
n = RAM[0]
i = 0
LOOP:
if (i>=n) goto END
RAM[addr] = -1
addr = addr+32
i++;
goto LOOP
END:
goto END
  @32
  D=A
  @addr
  M=D+M // addr = addr+32
  @i
  M=M+1 // i++
  @LOOP
  0; JMP // goto LOOP
  (END)
  @END
  0; JMP

## Slide 69: Example: draw a rectangle (assembly)
addr = SCREEN
n = RAM[0]
i = 0
LOOP:
if (i>=n) goto END
RAM[addr] = -1
addr = addr+32
i++;
goto LOOP
END:
goto END
  @32
  D=A
  @addr
  M=D+M // addr = addr+32
  @i
  M=M+1 // i++
  @LOOP
  0; JMP // goto LOOP
  (END)
  @END
  0; JMP

## Slide 70: Project #5: Computer-on-a-chip interface

## Slide 71: Computer-on-a-chip implementation
CHIP Computer {
IN reset;
PARTS:
// implementation missing
}
Implementation:
  You need to implement Memory and CPU first.
  Simple, the chip-parts do all the hard work.

## Slide 72: Perspective: from here to a “real” computer
Caching
More I/O units
Special-purpose processors (I/O, graphics, communications, …)
Multi-core / parallelism
Efficiency
Energy consumption considerations
And more ...