## Slide 1: Assembler
www.nand2tetris.org
Building a Modern Computer From First Principles
Notes: 1

## Slide 2: Where we are at:
Assembler
Chapter 6
H.L. Language
&
Operating Sys.
abstract interface
Compiler
Chapters 10 - 11
VM Translator
Chapters 7 - 8
Computer
Architecture
Chapters 4 - 5
Gate Logic
Chapters 1 - 3
Electrical
Engineering
Physics
Virtual
Machine
abstract interface
Software
hierarchy
Assembly
Language
abstract interface
Hardware
hierarchy
Machine
Language
abstract interface
Hardware
Platform
abstract interface
Chips &
Logic Gates
abstract interface
Human
Thought
Abstract design
Chapters 9, 12

## Slide 3: Why care about assemblers?
Assemblers employ nifty programming tricks
Assemblers are the first rung up the software hierarchy ladder
An assembler is a translator of a simple language
Writing an assembler = low-impact practice for writing compilers.
cross-platform
compiling

## Slide 4
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
...
Target code (a text file of binary Hack code)
assemble
Assembly example
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
... // Etc.
Source code (example)
The program translation challenge
Extract the program’s semantics from the source program, using the syntax rules of the source language
Re-express the program’s semantics in the target language, using the syntax rules of the target language
Assembler = simple translator
Translates each assembly command into one or more binary machine instructions
Handles symbols (e.g. i, sum, LOOP, …).
execute

## Slide 5: Revisiting Hack low-level programming: an example
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Assembly program (sum.asm)
CPU emulator screen shot after running this program
The CPU emulator allows loading and executing symbolic Hack code. It resolves all the symbolic symbols to memory locations, and executes the code.
program generated output
user supplied input

## Slide 6: The assembler’s view of an assembly program
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
Notes: 6

## Slide 7: The assembler’s view of an assembly program
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
White space
    Empty lines/indentation
    Line comments
    In-line comments
Notes: 7

## Slide 8: The assembler’s view of an assembly program
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
White space
    Empty lines/indentation
    Line comments
    In-line comments
Instructions
    A-instruction
    C-instruction
Notes: 8

## Slide 9: The assembler’s view of an assembly program
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
White space
    Empty lines/indentation
    Line comments
    In-line comments
Instructions
    A-instruction
    C-instruction
Symbols
    references
    Label declaration (XXX)
Notes: 9

## Slide 10: The assembler’s view of an assembly program
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@16
M=1 // i = 1
@17
M=0 // sum = 0
@16 // if i>RAM[0] goto WRITE
D=M
@0
D=D-M
@18
D;JGT
@16 // sum += i
D=M
@17
M=D+M
@16 // i++
M=M+1
@4 // goto LOOP
0;JMP
@17
D=M
@1
M=D // RAM[1] = the sum
@22
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
White space
    Empty lines/indentation
    Line comments
    In-line comments
Instructions
    A-instruction
    C-instruction
Symbols
    references
    Label declaration (XXX)
Assume that there is
no symbol for now!
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
Notes: 10

## Slide 11: White space
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@16
M=1 // i = 1
@17
M=0 // sum = 0
@16 // if i>RAM[0] goto WRITE
D=M
@0
D=D-M
@18
D;JGT
@16 // sum += i
D=M
@17
M=D+M
@16 // i++
M=M+1
@4 // goto LOOP
0;JMP
@17
D=M
@1
M=D // RAM[1] = the sum
@22
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
White space
    Empty lines/indentation
    Line comments
    In-line comments
Instructions
    A-instruction
    C-instruction
Symbols
    references
    Label declaration (XXX)
Notes: 11

## Slide 12: White space → ignore/remove them
@16
M=1
@17
M=0
@16
D=M
@0
D=D-M
@18
D;JGT
@16
D=M
@17
M=D+M
@16
M=M+1
@4
0;JMP
@17
D=M
@1
M=D
@22
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
White space
    Empty lines/indentation
    Line comments
    In-line comments
Instructions
    A-instruction
    C-instruction
Symbols
    references
    Label declaration (XXX)
Notes: 12

## Slide 13: Instructions → binary encoding
@16
M=1
@17
M=0
@16
D=M
@0
D=D-M
@18
D;JGT
@16
D=M
@17
M=D+M
@16
M=M+1
@4
0;JMP
@17
D=M
@1
M=D
@22
0;JMP
Assembly program
Assembly program = a stream of text lines, each being one of the following:
White space
    Empty lines/indentation
    Line comments
    In-line comments
Instructions
    A-instruction
    C-instruction
Symbols
    references
    Label declaration (XXX)
Notes: 13

## Slide 14: Translating / assembling A-instructions
Translation to binary:
If value is a non-negative decimal number, simple, e.g. @16
If value is a symbol, later.

## Slide 15: Translating / assembling C-instructions

## Slide 16: Translating / assembling C-instructions
Example: MD=D+1

## Slide 17: Translating / assembling C-instructions
Example: D; JGT

## Slide 18: The overall assembly logic
For each (real) command
Parse the command, i.e. break it into its underlying fields
A-instruction: replace the symbolic reference (if any) with the corresponding memory address, which is a number
(how to do it, later)
C-instruction: for each field in the instruction, generate the corresponding binary code
Assemble the translated binary codes into a complete 16-bit machine instruction
Write the 16-bit instruction to the output file.
// Computes 1+...+RAM[0]
// And stores the sum in RAM[1].
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Assembly program

## Slide 19
Assembly programs typically have many symbols:
Labels that mark destinations of goto commands
Labels that mark special memory locations
Variables
These symbols fall into two categories:
User–defined symbols (created by programmers)
  Variables
  Labels (forward reference could be a problem)
Pre-defined symbols (used by the Hack platform).
Handling symbols (aka symbol resolution)
@R0
D=M
@END
D;JLE
@counter
M=D
@SCREEN
D=A
@x
M=D
(LOOP)
@x
A=M
M=-1
@x
D=M
@32
D=D+A
@x
M=D
@counter
MD=M-1
@LOOP
D;JGT
(END)
@END
0;JMP
Typical symbolic Hack assembly code:
Notes: 19

## Slide 20
Label symbols: Used to label destinations of goto commands. Declared by the pseudo-command (XXX). This directive defines the symbol XXX to refer to the instruction memory location holding the next command in the program. (the assembler needs to maintain instrCtr)
Variable symbols: Any user-defined symbol xxx appearing in an assembly program that is not defined elsewhere using the (xxx) directive is treated as a variable, and is automatically assigned a unique RAM address, starting at RAM address 16 (the assembler needs to maintain nextAddr)
(why start at 16? Later.)
By convention, Hack programmers use lower-case and upper-case to represent variable and label names, respectively
Handling symbols: user-defined symbols
@R0
D=M
@END
D;JLE
@counter
M=D
@SCREEN
D=A
@x
M=D
(LOOP)
@x
A=M
M=-1
@x
D=M
@32
D=D+A
@x
M=D
@counter
MD=M-1
@LOOP
D;JGT
(END)
@END
0;JMP
Typical symbolic Hack assembly code:
Notes: 20

## Slide 21
Virtual registers: The symbols R0,…, R15 are automatically predefined to refer to RAM addresses 0,…,15
I/O pointers: The symbols SCREEN and KBD are automatically predefined to refer to RAM addresses 16384 and 24576, respectively (base addresses of the screen and keyboard memory maps)
VM control pointers: the symbols SP, LCL, ARG, THIS, and THAT (that don’t appear in the code example on the right) are automatically predefined to refer to RAM addresses 0 to 4, respectively
(The VM control pointers, which overlap R0,…, R4 will come to play in the virtual machine implementation, covered in the next lecture)
@R0
D=M
@END
D;JLE
@counter
M=D
@SCREEN
D=A
@x
M=D
(LOOP)
@x
A=M
M=-1
@x
D=M
@32
D=D+A
@x
M=D
@counter
MD=M-1
@LOOP
D;JGT
(END)
@END
0;JMP
Typical symbolic Hack assembly code:
Handling symbols: pre-defined symbols
Notes: 21

## Slide 22
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)
This symbol table is generated by the assembler, and used to translate the symbolic code into binary code.
Handling symbols: symbol table
R0 0
R1 1
R2 2
... ...
R15 15
SCREEN 16384
KBD 24576
SP 0
LCL 1
ARG 2
THIS 3
THAT 4
LOOP 4
WRITE 18
END 22
i 16
sum 17
Symbol table

## Slide 23
R0 0
R1 1
R2 2
...
R15 15
SCREEN 16384
KBD 24576
SP 0
LCL 1
ARG 2
THIS 3
THAT 4
Symbol table
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)
Initialization: create an empty symbol table and populate it with all the pre-defined symbols
Handling symbols: constructing the symbol table

## Slide 24
R0 0
R1 1
R2 2
...
R15 15
SCREEN 16384
KBD 24576
SP 0
LCL 1
ARG 2
THIS 3
THAT 4
LOOP 4
WRITE 18
END 22
Symbol table
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)
Initialization: create an empty symbol table and populate it with all the pre-defined symbols
First pass: go through the entire source code, and add all the user-defined label symbols to the symbol table (without generating any code)
Handling symbols: constructing the symbol table

## Slide 25
R0 0
R1 1
R2 2
...
R15 15
SCREEN 16384
KBD 24576
SP 0
LCL 1
ARG 2
THIS 3
THAT 4
LOOP 4
WRITE 18
END 22
i 16
sum 17
Symbol table
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)
Initialization: create an empty symbol table and populate it with all the pre-defined symbols
First pass: go through the entire source code, and add all the user-defined label symbols to the symbol table (without generating any code)
Second pass: go again through the source code, and use the symbol table to translate all the commands. In the process, handle all the user-defined variable symbols.
Handling symbols: constructing the symbol table

## Slide 26
R0 0
R1 1
R2 2
...
R15 15
SCREEN 16384
KBD 24576
SP 0
LCL 1
ARG 2
THIS 3
THAT 4
Symbol table
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)
Handling symbols: constructing the symbol table (one-pass solution?)

## Slide 27: The assembly process (detailed)
Initialization: create the symbol table and initialize it with the pre-defined symbols
First pass: march through the source code without generating any code. For each label declaration (LABEL) that appears in the source code, add the pair <LABEL , n > to the symbol table

## Slide 28: The assembly process (detailed)
Second pass: march again through the source, and process each line:
  If the line is a C-instruction, simple
  If the line is @xxx where xxx is a number, simple
  If the line is @xxx and xxx is a symbol, look it up in the symbol table and proceed as follows:
    If the symbol is found, replace it with its numeric value and complete the command’s translation
    If the symbol is not found, then it must represent a new variable: add the pair <xxx , n > to the symbol table, where n is the next available RAM address, and complete the command’s translation.
    (Platform design decision: the allocated RAM addresses are running, starting at address 16).

## Slide 29
Note that comment lines and pseudo-commands (label declarations) generate no code.
0000000000010000
1110111111001000
0000000000010001
1110101010001000
0000000000010000
1111110000010000
0000000000000000
1111010011010000
0000000000010010
1110001100000001
0000000000010000
1111110000010000
0000000000010001
1111000010001000
0000000000010000
1111110111001000
0000000000000100
1110101010000111
0000000000010001
1111110000010000
0000000000000001
1110001100001000
0000000000010110
1110101010000111
Target code
assemble
The result ...
// Computes 1+...+RAM[0]
// And stored the sum in RAM[1]
@i
M=1 // i = 1
@sum
M=0 // sum = 0
(LOOP)
@i // if i>RAM[0] goto WRITE
D=M
@R0
D=D-M
@WRITE
D;JGT
@i // sum += i
D=M
@sum
M=D+M
@i // i++
M=M+1
@LOOP // goto LOOP
0;JMP
(WRITE)
@sum
D=M
@R1
M=D // RAM[1] = the sum
(END)
@END
0;JMP
Source code (example)

## Slide 30: Proposed assembler implementation
An assembler program can be written in any high-level language. (and could be run in the other platforms, cross-platform compiling)
The book proposes a language-independent design, as follows.
Software modules:
Parser: Unpacks each command into its underlying fields
Code: Translates each field into its corresponding binary value, and assembles the resulting values
SymbolTable: Manages the symbol table
Main: Initializes I/O files and drives the show.

## Slide 31: Perspective
Simple machine language, simple assembler
Most assemblers are not stand-alone, but rather encapsulated in a translator of a higher order
C programmers that understand the code generated by a C compiler can improve their code considerably
C programming (e.g. for real-time systems) may involve re-writing critical segments in assembly, for optimization
Writing an assembler is an excellent practice for writing more challenging translators, e.g. a VM Translator and a compiler, as we will do in the next lectures.