## Slide 1: Boolean logic
Introduction to Computer
Yung-Yu Chuang
with slides by Sedgewick & Wayne (introcs.cs.princeton.edu), Nisan & Schocken (www.nand2tetris.org) and Harris & Harris (DDCA)

## Slide 2: Boolean Algebra
George Boole
1815 - 1864
Based on symbolic logic, designed by George Boole
Boolean variables take values as 0 or 1.
Boolean expressions created from:
  NOT, AND, OR

## Slide 3: NOT
Digital gate diagram for NOT:
X
X’
X


## Slide 4: AND
Digital gate diagram for AND:
XY
XY
XY

## Slide 5: OR
Digital gate diagram for OR:
X+Y
XY

## Slide 6: Operator Precedence
Examples showing the order of operations: NOT > AND > OR
Use parentheses to avoid ambiguity

## Slide 7: Defining a function
Description: square of x minus 1
Algebraic form : x2-1
Enumeration:
x | f(x)
1 | 0
2 | 3
3 | 8
4 | 15
5 | 24
: | :

## Slide 8: Defining a function
Description: number of days of the x-th month of a non-leap year
Algebraic form: ?
Enumeration:
x | f(x)
1 | 31
2 | 28
3 | 31
4 | 30
5 | 31
6 | 30
7 | 31
8 | 31
9 | 30
10 | 31
11 | 30
12 | 31

## Slide 9: Truth Table
Truth table.
  Systematic method to describe Boolean function.
  One row for each possible input combination.
  N inputs  2N rows.
AND truth table
0
0
0
1
1
0
1
1
0
0
0
1
x
y
x y
Notes: this is one Boolean function of two inputs. A systematic way to enumerate all input combinations is to count in binary.

## Slide 10: Proving the equivalence of two functions
Prove that x2-1=(x+1)(x-1)
Using algebra: (you need to follow some rules)
(x+1)(x-1) = x2+x-x-1= x2-1
Using enumeration:
x | (x+1)(x-1) | x2-1
1 | 0 | 0
2 | 3 | 3
3 | 8 | 8
4 | 15 | 15
5 | 24 | 24
: | : | :

## Slide 11: Important laws
x + 1 = 1
x + 0 = x
x + x = 1
x．1 = x
x．0 = 0
x．x = 0
DeMorgan Law
x．y = x + y
x + y = y + x
x + (y+z) = (x+y) + z
x．y = y．x
x．(y．z) = (x．y)．z
x．(y+z) = xy + xz

## Slide 12: Simplifying Boolean expressions
Example 1
Y = AB + AB

## Slide 13: Simplifying Boolean expressions
Example 1
Y = AB + AB
= B(A + A)
= B(1)
= B

## Slide 14: Simplifying Boolean expressions
Example 2
Y = A(AB + ABC)

## Slide 15: Simplifying Boolean expressions
Example 2
Y = A(AB + ABC)
= A(AB(1 + C))
= A(AB(1))
= A(AB)
= (AA)B
= AB

## Slide 16: DeMorgan’s Theorem
Y = AB = A + B
Y = A + B = A B

## Slide 17: Bubble pushing
Backward:
  Body changes
  Adds bubbles to inputs
Forward:
  Body changes
  Adds bubble to output

## Slide 18: Bubble pushing
What is the Boolean expression for this circuit?

## Slide 19: Bubble pushing
What is the Boolean expression for this circuit?
Y = AB + CD

## Slide 20: Bubble pushing rules
Begin at output, then work toward inputs
Push bubbles on final output back
Draw gates in a form so bubbles cancel

## Slide 21: Bubble pushing example

## Slide 22: Bubble pushing example

## Slide 23: Bubble pushing example

## Slide 24: Bubble pushing example

## Slide 25: Truth Tables
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: x  y
x | y | x  y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 26: Truth Tables
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: x  y
x | y | x | x  y
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 27: Truth Tables
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: x  y
x | y | x | x  y
0 | 0 | 1 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 1 | 0 | 1

## Slide 28: Truth Tables
Example: X  Y
x | y | y | xy
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 29: Truth Tables
Example: X  Y
x | y | y | xy
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0

## Slide 30: Truth Tables (3 of 3)
When S=0, return X; otherwise, return Y.
Example: (Y  S)  (X  S)
Two-input multiplexer
S | X | Y | YS | S | XS | (Y  S)  (X  S)
0 | 0 | 0 |  |  |  | 
0 | 0 | 1 |  |  |  | 
0 | 1 | 0 |  |  |  | 
0 | 1 | 1 |  |  |  | 
1 | 0 | 0 |  |  |  | 
1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  | 
1 | 1 | 1 |  |  |  | 

## Slide 31: Truth Tables (3 of 3)
When S=0, return X; otherwise, return Y.
Example: (Y  S)  (X  S)
Two-input multiplexer
S | X | Y | YS | S | XS | (Y  S)  (X  S)
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 1

## Slide 32: Truth Table for Functions of 2 Variables
2 variables lead to four possible combinations
A 2-variable function f has to define four values
f
y
0
V00
0
1
V01
1
0
V10
1
1
V11
x
0

## Slide 33: Truth Table for Functions of 2 Variables
Truth table.
  16 Boolean functions of 2 variables.
ZERO
Truth table for all Boolean functions of 2 variables
y
0
0
0
1
0
1
0
0
1
1
0
0
0
1
0
0
1
0
0
x
0
0
1
1
AND
0
0
0
1
y
0
1
0
1
XOR
0
1
1
0
OR
0
1
1
1
x
0
NOR
Truth table for all Boolean functions of 2 variables
y
0
1
0
1
0
1
0
0
1
1
0
y'
1
0
1
0
x'
1
1
0
0
1
0
1
1
EQ
1
0
0
1
1
1
0
1
NAND
1
1
1
0
ONE
1
1
1
1
x
0
every 4-bit value represents one
Notes: Let's look at some other functions. ZERO function not very exciting.
Can enumerate all boolean *functions* of N variables by counting in binary too!

## Slide 34: All Boolean functions of 2 variables

## Slide 35: Truth Table for Functions of 3 Variables
Truth table.
  16 Boolean functions of 2 variables.
  256 Boolean functions of 3 variables.
  2^(2^n) Boolean functions of n variables!
AND
some functions of 3 variables
z
0
0
0
1
0
1
0
0
1
1
0
y
0
x
0
0
0
0
0
0
1
1
0
1
1
0
1
1
1
1
0
0
0
1
OR
0
1
1
1
1
1
1
1
MAJ
0
0
0
1
0
1
1
1
ODD
0
1
1
0
1
0
0
1
every 4-bit value represents one
every 8-bit value represents one
every 2n-bit value represents one
Notes: if N = 10, there are roughly 2^2^10 ~ 2^1000 possible circuits. No computer will ever see all of these. We choose the "good" ones.

## Slide 36: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
proves that { AND, OR, NOT } are universal
z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1

## Slide 37: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
proves that { AND, OR, NOT } are universal
z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
expressing MAJ using sum-of-products

## Slide 38: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
proves that { AND, OR, NOT } are universal
z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
expressing MAJ using sum-of-products

## Slide 39: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
proves that { AND, OR, NOT } are universal
z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
0
0
0
1
0
0
0
0
expressing MAJ using sum-of-products

## Slide 40: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
proves that { AND, OR, NOT } are universal
z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
x'yz
0
0
0
1
0
0
0
0
expressing MAJ using sum-of-products

## Slide 41: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
proves that { AND, OR, NOT } are universal
z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
x'yz
0
0
0
1
0
0
0
0
xy'z
0
0
0
0
0
1
0
0
expressing MAJ using sum-of-products

## Slide 42: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
x'yz
expressing MAJ using sum-of-products
z
xyz'
xyz
xy'z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
proves that { AND, OR, NOT } are universal

## Slide 43: Sum-of-Products
Sum-of-products. Systematic procedure for representing a Boolean function using AND, OR, NOT.
  Form AND term for each 1 in Boolean function.
  OR terms together.
x'yz
expressing MAJ using sum-of-products
z
xyz'
xyz
xy'z
MAJ
y
x
0
0
0
1
0
1
1
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1
x'yz + xy'z + xyz' + xyz
0
0
0
1
0
1
1
1
proves that { AND, OR, NOT } are universal

## Slide 44: Universality of AND, OR, NOT
Fact. Any Boolean function can be expressed using AND, OR, NOT.
  { AND, OR, NOT } are universal.
  Ex: XOR(x,y) = xy' + x'y.
x'
Expressing XOR Using AND, OR, NOT
y
0
1
1
1
0
0
1
0
x'y
0
1
0
0
x'y + xy'
0
1
1
0
xy'
0
0
1
0
y'
1
0
1
0
x XOR y
0
1
1
0
x
0
0
1
1
NOT x
x'
x AND y
x y
x OR y
Meaning
Notation
x + y
Notes: AND, OR, NOT universal means any Boolean function can be made from these gates.
Stresses importance of developing good abstractions.

## Slide 45: Universality of AND, OR, NOT
Fact. Any Boolean function can be expressed using AND, OR, NOT.
  { AND, OR, NOT } are universal.
  Ex: XOR(x,y) = xy' + x'y.
Exercise. Show {AND, NOT}, {OR, NOT}, {NAND}, {NOR} are universal.
Hint. DeMorgan's law: (x'y')' = x + y.
x'
Expressing XOR Using AND, OR, NOT
y
0
1
1
1
0
0
1
0
x'y
0
1
0
0
x'y + xy'
0
1
1
0
xy'
0
0
1
0
y'
1
0
1
0
x XOR y
0
1
1
0
x
0
0
1
1
NOT x
x'
x AND y
x y
x OR y
Meaning
Notation
x + y
Notes: AND, OR, NOT universal means any Boolean function can be made from these gates.
Stresses importance of developing good abstractions.

## Slide 46: {AND, NOT} is universal

## Slide 47: {NAND} is universal

## Slide 48: From Math to Real-World implementation
We can implement any Boolean function using NAND gates only.
We talk about abstract Boolean algebra (logic) so far.
Is it possible to realize it in real world?
The technology needs to permit switching and conducting. It can be built using magnetic, optical, biological, hydraulic and pneumatic mechanism.

## Slide 49: Implementation of gates
Fluid switch
(http://www.cs.princeton.edu/introcs/lectures/fluid-computer.swf)

## Slide 50: Digital Circuits
What is a digital system?
  Analog: signals vary continuously.
  Digital: signals are 0 or 1.
Why digital systems?
  Accuracy and reliability.
  Staggeringly fast and cheap.
Basic abstractions.
  On, off.
  Wire: propagates on/off value.
  Switch: controls propagation of on/off values through wires.
0.0V
0.5V
2.8V
3.3V
0
1
0
Notes: Digital – could in principle take on a discrete set of values, but typically 0/1 (binary)
tiny abstraction, but not obvious this was the right choice (0/1 T/F)
scientists considered analog machines initially (more complicated interface)

## Slide 51: Wires
Wires.
  On (1): connected to power.
  Off (0): not connected to power.
  If a wire is connected to a wire that is on, that wire is also on.
  Typical drawing convention: "flow" from top, left to bottom, right.
0
power connection
1
1
1
Notes: logical values = information

## Slide 52: Controlled Switch
Controlled switch. [relay implementation]
  3 connections: input, output, control.
  Magnetic force pulls on a contact that cuts electrical flow.
  Control wire affects output wire, but output does not affect control; establishes forward flow of information over time.
X
X
Notes: computers are not intrinsically electrical or based on silicon technology: from "The Pattern on the Stone"
water pressure is used to distinguish between two possible signals
amplification: even if input is a little low on pressure due to a leaky pipe, output is always at full pressure as long as signal is strong enough to move valve
restoring logic: gradual decrease in pressure not a problem

## Slide 53: Relay

## Slide 54: Circuit Anatomy
Notes: logical values = information

## Slide 55: Logic Gates: Fundamental Building Blocks
Notes: Gates will be used as building block for larger, more complicated, circuit elements.
NOT also called "inverter".
think abstractly (although these abstractions correspond directly with physical world)

## Slide 56: NOT

## Slide 57: NOT
1
0
0
1

## Slide 58: OR

## Slide 59: Series relays = NOR
0
1
0
0
1
0
1
1
0
0
0
1

## Slide 60: OR

## Slide 61: AND

## Slide 62: AND

## Slide 63: Logic Gates: Fundamental Building Blocks
Notes: Gates will be used as building block for larger, more complicated, circuit elements.
NOT also called "inverter".
think abstractly (although these abstractions correspond directly with physical world)

## Slide 64: What about parallel relays?
0
1
1
0
0
1
=NAND

## Slide 65: Can we implement AND/OR using parallel relays?
Now we know how to implement AND,OR and NOT. We can just use them as black boxes without knowing how they were implemented. Principle of information hiding.

## Slide 66: Multiway Gates
Multiway gates.
  OR: 1 if any input is 1; 0 otherwise.
  AND: 1 if all inputs are 1; 0 otherwise.
  Generalized: negate some inputs.
Notes: wire carries output of one gate to the input(s) of others. Only one output per wire.

## Slide 67: Multiway Gates
Multiway gates.
  OR: 1 if any input is 1; 0 otherwise.
  AND: 1 if all inputs are 1; 0 otherwise.
  Generalized: negate some inputs.
Notes: wire carries output of one gate to the input(s) of others. Only one output per wire.

## Slide 68: Multiway Gates
Multiway gates.
  Can also be built from 2-way gates (less efficient but implementation independent)
  Example: build 4-way OR from 2-way ORs
Notes: wire carries output of one gate to the input(s) of others. Only one output per wire.

## Slide 69: Translate Boolean Formula to Boolean Circuit
Sum-of-products. XOR.

## Slide 70: Translate Boolean Formula to Boolean Circuit
Sum-of-products. XOR.

## Slide 71: Translate Boolean Formula to Boolean Circuit
Sum-of-products. XOR.

## Slide 72: Gate logic
Xor(a,b) = Or(And(a,Not(b)),And(Not(a),b)))
Implementation
Interface

## Slide 73: Expressing a Boolean Function Using AND, OR, NOT
Ingredients.
  AND gates.
  OR gates.
  NOT gates.
  Wire.
Instructions.
  Step 1: represent input and output signals with Boolean variables.
  Step 2: construct truth table to carry out computation.
  Step 3: derive (simplified) Boolean expression using sum-of products.
  Step 4: transform Boolean expression into circuit.

## Slide 74: Translate Boolean Formula to Boolean Circuit
Sum-of-products. Majority.

## Slide 75: Translate Boolean Formula to Boolean Circuit
Sum-of-products. Majority.

## Slide 76: Translate Boolean Formula to Boolean Circuit
Sum-of-products. Majority.

## Slide 77: Translate Boolean Formula to Boolean Circuit
Sum-of-products. Majority.

## Slide 78: ODD Parity Circuit
ODD(x, y, z).
  1 if odd number of inputs are 1.
  0 otherwise.
Notes: let's use the recipe
generalizes XOR

## Slide 79: ODD Parity Circuit
ODD(x, y, z).
  1 if odd number of inputs are 1.
  0 otherwise.
x'y'z
Expressing ODD using sum-of-products
z
xy'z'
xyz
x'yz'
ODD
y
x
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
1
0
0
1
1
0
0
1
1
0
0
0
0
1
1
1
1
0
1
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
1
x'y'z + x'yz' + xy'z' + xyz
0
1
1
0
1
0
0
1
Notes: let's use the recipe
generalizes XOR

## Slide 80: ODD Parity Circuit
ODD(x, y, z).
  1 if odd number of inputs are 1.
  0 otherwise.
Notes: but this one can't be simplified (take it from Doug)

## Slide 81: ODD Parity Circuit
ODD(x, y, z).
  1 if odd number of inputs are 1.
  0 otherwise.
Notes: but this one can't be simplified (take it from Doug)

## Slide 82: Simplification Using Boolean Algebra
Every function can be written as sum-of-product
Many possible circuits for each Boolean function.
  Sum-of-products not necessarily optimal in:
    number of switches (space)
    depth of circuit (time)
Notes: Don't worry about simplifications in COS 126 – just know that they exist.
This mattered a lot in ancient times. Not so important now. Uniformity more critical. Lay down a "sum-of-products" grid. Just burn in the NOT gates.

## Slide 83: Boolean expression simplification
Karnaugh map

## Slide 84: Karnaugh Maps (K-Maps)
Boolean expressions can be minimized by combining terms
K-maps minimize equations graphically
PA + PA = P

## Slide 85: K-Map
Circle 1’s in adjacent squares
In Boolean expression, include only literals whose true and complement form are not in the circle
Y = AB

## Slide 86: 3-Input K-Map

## Slide 87: 3-Input K-Map
Y = AB + BC

## Slide 88: K-Map Rules
Every 1 must be circled at least once
Each circle must span a power of 2 (i.e. 1, 2, 4) squares in each direction
Each circle must be as large as possible
A circle may wrap around the edges
A “don't care” (X) is circled only if it helps minimize the equation

## Slide 89: 4-Input K-Map

## Slide 90: 4-Input K-Map

## Slide 91: 4-Input K-Map

## Slide 92: 4-Input K-Map with Don‘t care

## Slide 93: 4-Input K-Map with Don‘t care

## Slide 94: 4-Input K-Map with Don‘t care

## Slide 95: Example
xy
z

## Slide 96: Simplification Using Boolean Algebra
Many possible circuits for each Boolean function.
  Sum-of-products not necessarily optimal in:
    number of switches (space)
    depth of circuit (time)
  MAJ(x, y, z) = x'yz + xy'z + xyz' + xyz = xy + yz + xz.
Notes: Don't worry about simplifications in COS 126 – just know that they exist.
This mattered a lot in ancient times. Not so important now. Uniformity more critical. Lay down a "sum-of-products" grid. Just burn in the NOT gates.

## Slide 97: Layers of Abstraction
Layers of abstraction.
  Build a circuit from wires and switches. [implementation]
  Define a circuit by its inputs and outputs. [API]
  To control complexity, encapsulate circuits. [ADT]
Notes: logical values = information

## Slide 98: Layers of Abstraction
Layers of abstraction.
  Build a circuit from wires and switches. [implementation]
  Define a circuit by its inputs and outputs. [API]
  To control complexity, encapsulate circuits. [ADT]
Notes: logical values = information

## Slide 99: Building a chip
?
Xor
a
b
out
if ((a == 0 and b == 1) or (a == 1 and b == 0))
sets out = 1
else
sets out = 0
The process
Design the chip architecture
Specify the architecture in HDL
Test the chip in a hardware simulator
Optimize the design
Realize the optimized design in silicon.

## Slide 100: Building a chip
?
Xor
a
b
out
if ((a == 0 and b == 1) or (a == 1 and b == 0))
sets out = 1
else
sets out = 0
The process
Design the chip architecture
Specify the architecture in HDL
Test the chip in a hardware simulator
Optimize the design
Realize the optimized design in silicon.

## Slide 101: Chip design
  Step 1: identify input and output
  Step 2: construct truth table
  Step 3: derive (simplified) Boolean expression using sum-of products.
  Step 4: transform Boolean expression into circuit/implement it using HDL.
You would like to test the gate before packaging.

## Slide 102: XOR
a | b | out
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 103: Chip interfaces
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in= , out= );
Not (in= , out= );
And (a= , b=, out=);
And (a= , b=, out=);
Or (a= , b=, out=);
}
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a
If I want to use some chip-parts, how do I figure out their signatures?

## Slide 104: Chip interfaces: Hack chip set API
Add16 (a= ,b= ,out= );
ALU (x= ,y= ,zx= ,nx= ,zy= ,ny= ,f= ,no= ,out= ,zr= ,ng= );
And16 (a= ,b= ,out= );
And (a= ,b= ,out= );
Aregister (in= ,load= ,out= );
Bit (in= ,load= ,out= );
CPU (inM= ,instruction= ,reset= ,outM= ,writeM= ,addressM= ,pc= );
DFF (in= ,out= );
DMux4Way (in= ,sel= ,a= ,b= ,c= ,d= );
DMux8Way (in= ,sel= ,a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= );
Dmux (in= ,sel= ,a= ,b= );
Dregister (in= ,load= ,out= );
FullAdder (a= ,b= ,c= ,sum= ,carry= );
HalfAdder (a= ,b= ,sum= , carry= );
Inc16 (in= ,out= );
Keyboard (out= );
Memory (in= ,load= ,address= ,out= );
Mux16 (a= ,b= ,sel= ,out= );
Mux4Way16 (a= ,b= ,c= ,d= ,sel= ,out= );
Mux8Way16 (a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= ,sel= ,out= );
Mux8Way (a= ,b= ,c= ,d= ,e= ,f= ,g= ,h= ,sel= ,out= );
Mux (a= ,b= ,sel= ,out= );
Nand (a= ,b= ,out= );
Not16 (in= ,out= );
Not (in= ,out= );
Or16 (a= ,b= ,out= );
Or8Way (in= ,out= );
Or (a= ,b= ,out= );
PC (in= ,load= ,inc= ,reset= ,out= );
PCLoadLogic (cinstr= ,j1= ,j2= ,j3= ,load= ,inc= );
RAM16K (in= ,load= ,address= ,out= );
RAM4K (in= ,load= ,address= ,out= );
RAM512 (in= ,load= ,address= ,out= );
RAM64 (in= ,load= ,address= ,out= );
RAM8 (in= ,load= ,address= ,out= );
Register (in= ,load= ,out= );
ROM32K (address= ,out= );
Screen (in= ,load= ,address= ,out= );
Xor (a= ,b= ,out= );
Open the Hack chip set API in a window, and copy-paste chip signatures into your HDL code, as needed

## Slide 105: Built-in chips
CHIP Foo {
IN ...;
OUT ...;
PARTS:
...
Bar(...)
...
}
Forcing the simulator to use a built-in chip, say Bar:
Typically, Bar.hdl will be either a given stub-file, or a file that has an incomplete implementation
Remove, or rename, the file Bar.hdl from the project folder
Whenever Bar will be mentioned as a chip-part in some chip definition, the simulator will fail to find Bar.hdl in the current folder. This will cause the simulator to invoke the built-in version of Bar instead.
Q: Suppose you want to use a chip-part before you’ve implemented it. How to do it?
A: The simulator features built-in implementations of all the project 1 chips

## Slide 106: Design: Requirements
a | b | out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Requirement
Build a chip that delivers this functionality
if ((a == 0 and b == 1) or (a == 1 and b == 0))
sets out = 1
else
sets out = 1
Gate Interface
Expressed as an HDL stub file
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Missing implementation
Xor
a
b
out

## Slide 107: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Missing implementation
Gate Interface
Expressed as an HDL stub file

## Slide 108: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Missing implementation
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a
Gate Interface
Expressed as an HDL stub file
Gate diagram

## Slide 109: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Missing implementation
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a
Gate diagram
Gate Interface
Expressed as an HDL stub file

## Slide 110: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
// Missing implementation
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a

## Slide 111: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
}
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a

## Slide 112: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
}
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a
Practice: Complete the missing HDL code

## Slide 113: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a

## Slide 114: Design: Implementation
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
a
Not
Not
And
And
Or
b
out
nota
notb
aAndNotb
notaAndb
out
b
a
b
a
in
in
out
out
out
out
b
a
gate
interface
gate
Implement-ation
A logic gate has:
One interface
Many possible implementations

## Slide 115: Hardware description languages
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
Observations:
HDL is a functional / declarative language
An HDL program can be viewed as a textual specification of a chip diagram
The order of HDL statements is insignificant.

## Slide 116: Hardware description languages
/** Sets out = (a And Not(b)) Or (Not(a) And b)) */
CHIP Xor {
IN a, b;
OUT out;
PARTS:
Not (in=a, out=nota);
Not (in=b, out=notb);
And (a=a, b=notb, out=aAndNotb);
And (a=nota, b=b, out=notaAndb);
Or (a=aAndNotb, b=notaAndb, out=out);
}
Common HDLs
VHDL
Verilog
…
Our HDL
Similar in spirit to other HDLs
Minimal and simple
Provides all you need for this course
  Our HDL Guide / Documentation:
  The Elements of Computing Systems / Appendix 2: HDL

## Slide 117: Multi-bit bus
LSB = Least significant bit
MSB = Most significant bit
13
12
15
14
9
8
11
10
5
4
7
6
1
0
3
2
Example: 16-bit bus
0
0
1
0
0
0
1
0
0
1
1
1
0
1
1
1
Sometimes we wish to manipulate a sequence of bits as a single entity
Such a multi-bit entity is termed “bus”

## Slide 118: Working with buses: Example
/* Adds two 16-bit values. */
CHIP Adder {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
/* Adds three 16-bit inputs. */
CHIP Adder3Way {
IN a[16], b[16], c[16];
OUT out[16];
out:
0
. . .
1
1
a:
1
0
1
15
. . .
. . .
1
1
b:
0
. . .
0
1
c:
1
. . .
0
0

## Slide 119: Working with buses: Example
/* Adds two 16-bit values. */
CHIP Adder {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
/* Adds three 16-bit inputs. */
CHIP Adder3Way {
IN a[16], b[16], c[16];
OUT out[16];
PARTS:
Adder(a= , b= , out= );
Adder(a= , b= , out= );
}
out:
0
. . .
1
1
a:
1
0
1
15
. . .
. . .
1
1
b:
0
. . .
0
1
c:
1
. . .
0
0

## Slide 120: Working with buses: Example
/* Adds two 16-bit values. */
CHIP Adder {
IN a[16], b[16];
OUT out[16];
PARTS:
...
}
/* Adds three 16-bit inputs. */
CHIP Adder3Way {
IN a[16], b[16], c[16];
OUT out[16];
PARTS:
Adder(a=a , b=b, out=ab);
Adder(a=ab, b=c, out=out);
}
out:
0
. . .
1
1
a:
1
0
1
15
. . .
. . .
1
1
b:
0
. . .
0
1
c:
1
. . .
0
0
n-bit value (bus) can be treated as a single entity
Creates an internal bus pin (ab)

## Slide 121: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
a:
1
0
1
3
2
1
0
1
out:
0
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;

## Slide 122: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a= , b= , out= );
And(a= , b= , out= );
And(a= , b= , out= );
}
a:
1
0
1
3
2
1
0
1
out:
0

## Slide 123: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a=a[0], b=a[1], out=and01);
And(a=and01, b=a[2], out=and012);
And(a=and012, b=a[3], out=out);
}
Input bus pins can be subscripted.
a:
1
0
1
3
2
1
0
1
out:
0

## Slide 124: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a=a[0], b=a[1], out=and01);
And(a=and01, b=a[2], out=and012);
And(a=and012, b=a[3], out=out);
}
Input bus pins can be subscripted.
a:
1
0
1
3
2
1
0
1
out:
0
/* Bit-wise And of two 4-bit inputs */
CHIP And4 {
IN a[4], b[4];
OUT out[4];
a:
1
0
1
3
2
1
0
0
b:
1
0
0
1
out:
1
0
0
0

## Slide 125: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
/* Bit-wise And of two 4-bit inputs */
CHIP And4 {
IN a[4], b[4];
OUT out[4];
PARTS:
And(a= , b= , out= );
And(a= , b= , out= );
And(a= , b= , out=. );
And(a= , b= , out= );
}
a:
1
0
1
3
2
1
0
0
b:
1
0
0
1
out:
1
0
0
0
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a=a[0], b=a[1], out=and01);
And(a=and01, b=a[2], out=and012);
And(a=and012, b=a[3], out=out);
}
Input bus pins can be subscripted.
a:
1
0
1
3
2
1
0
1
out:
0

## Slide 126: Working with individual bits within buses
/* Returns 1 if a==1 and b==1,
* 0 otherwise. */
CHIP And {
IN a, b;
OUT out;
...
}
/* Bit-wise And of two 4-bit inputs */
CHIP And4 {
IN a[4], b[4];
OUT out[4];
PARTS:
And(a=a[0], b=b[0], out=out[0]);
And(a=a[1], b=b[1], out=out[1]);
And(a=a[2], b=b[2], out=out[2]);
And(a=a[3], b=b[3], out=out[3]);
}
Output bus pins can be subscripted
a:
1
0
1
3
2
1
0
0
b:
1
0
0
1
out:
1
0
0
0
/* 4-way And: Ands 4 bits. */
CHIP And4Way {
IN a[4];
OUT out;
PARTS:
And(a=a[0], b=a[1], out=and01);
And(a=and01, b=a[2], out=and012);
And(a=and012, b=a[3], out=out);
}
Input bus pins can be subscripted.
a:
1
0
1
3
2
1
0
1
out:
0

## Slide 127: Hardware simulator (demonstrating Xor gate construction)
test script
HDL program

## Slide 128: Hardware simulator
HDL program

## Slide 129: Hardware simulator
HDL program
output file

## Slide 130: Project materials: www.nand2tetris.org
Project 1 web site
And.hdl , And.tst , And.cmp files

## Slide 131: Project 1 tips
Read the Introduction + Chapter 1 of the book
Download the book’s software suite
Go through the hardware simulator tutorial
Do Project 0 (optional)
You’re in business.

## Slide 132: Gates for project #1 (Basic Gates)

## Slide 133: Gates for project #1

## Slide 134: Gates for project #1 (Multi-bit version)

## Slide 135: Gates for project #1 (Multi-way version)

## Slide 136: Gates for project #1 (Multi-way version)

## Slide 137: Gates for project #1 (Multi-way version)

## Slide 138: Gates for project #1 (Multi-way version)