## Slide 1: Hsin-Mu (Michael) Tsai (蔡欣穆)
12pt Medium Subhead

## Slide 2: Vehicular Visible Light Communications
IoV: Cooperation between Vehicles
  Building Roads: No Moore’s Law Here
  Increase Road and Energy Efficiency
Challenges: V2V Communications
  Challenge 1: Density and Speed
  Challenge 2:Who is Speaking?
  Challenge 3: Cost and Benefit
Vehicular Visible Light Communications
  Keep the Light’s Original Function
  Receiver Options
  V2LC for Scooter Safety
Conclusion

## Slide 3
http://www.forcegt.com/wp-content/uploads/2012/09/volvo_road_train-11.jpg
IoV: Cooperation between Vehicles

## Slide 4: Building Roads: No Moore’s Law Here
Wugu-Yangmei Overpass (completed in 2013)
(for Freeway No. 1 in Taiwan)
  Cost: 3B USD for 40 km of elevated road
    The most expensive (per unit length) in the history
  Divert approximately 25% of traffic from the original highway
  Improve rush hour average speed:
    40-50 kmph → 80-90 kmph
http://twimg.edgesuite.net//images/twapple/640pix/20121217/LN06/LN06_004.jpg

## Slide 5: Increase Road and Energy Efficiency
At 100 km/h, the road surface utilization = 5%
Reduce the gap - Longitudinal control (adaptive cruise control)
Reduce lane width - Automatic steering
Reduce aerodynamic drag - Close-formation automated platoons can save 10% to 20% of total energy use
Only possible through cooperation with communications
  Drivers’ response delays cause stop and go disturbances
45.5 m
5 m
3.5 m
1.8 m

## Slide 6
http://img.autonet.com.tw/news/img/2012/8/bb20802621.jpg
Challenges: V2V Communications

## Slide 7: Challenge 1: Density and Speed
Range →reaction time
200 km/h relative speed 100 m = 1.8 s @ 200 km/h
A 100-m road segment can have:
  More than 600 scooters
  More than 120 cars
Heavy Interference
The need for reliable communications
Notes: 100/2 = 50* 3*2 = 300

## Slide 8: Challenge 2:Who is Speaking?
My location is (X3, Y3) and my speed is 98 mph, and I am braking.
My location is (X2, Y2) and my speed is 101 mph.
My location is (X1, Y1) and my speed is 106 mph.
GPS Uncertainty = 5 -10 m
Is the car in front of me braking?

## Slide 9: Challenge 3: Cost and Benefit
DSRC (IEEE 802.11p) – the current dominant standard for vehicular communications
NOT in vehicle products today
Low adoption incentive: where is the (day 1) benefit?
  Minimum market penetration rate: 10% (All new cars have it have to wait for 2 years)
Low adoption incentive: high initial cost
  Complexity similar to a WiFi radio
  But with much lower quantity, when bootstrapping the market

## Slide 10
EE Times: Top 10 Automotive Agendas for 2014 & Beyond
7. Time to act on V2V,V2I
Vehicular Visible Light Communications

## Slide 11: Vehicular Visible Light Communications

## Slide 12: Keep the Light’s Original Function

## Slide 13: Receiver Options
 | Data Rate | Number of pixels | Cost
Photodiode module | Up to several Mb/s | 1 | Extra
Camera sensor | A few Bytes/s | Millions | Use existing cameras

## Slide 14: V2LC for Scooter Safety
S.-H. You, S.-H. Chang, H.-M. Lin, H.-M. Tsai, "Demo: Visible Light Communications for Scooter Safety,“ ACM MobiSys, Taipei, Taiwan, June 2013
Video: http://goo.gl/lo1f9

## Slide 15: Automatic Interference Filtering
!
!
!
!
!
!
Your Car
Visible light cannot penetrate obstacles = line-of-sight only
VLC communication coverage = immediate neighbors only
 only those that could immediately collide with you
Comparison: RF coverage includes a lot more irrelevant vehicles  additional interference  less reliable
RF Coverage
VLC Coverage
Automatic interference filtering with VLC  Zero delay + zero overhead  Always scalable to density & speed*!
*S.-H. You, O. Shih, N. Wisitpongphan, H.-M. Tsai, and R. D. Roberts, “Smart Automotive Lighting for Vehicle Safety,” IEEE Communications, vol.51, no.12, pp. 50-59, December 2013.
Challenge 1

## Slide 16: Highly Directional Transmission
Easily regulated output radiation pattern Highly directional transmission with minimal leakage
Scooter Tail Light
Radiation Pattern
T
Safety regulation specifies the minimum light intensity (at 30.48 m) within 20 degrees of irradiance angle.
W. Viriyasitavat, S.-H. Yu, and H.-M. Tsai, “Short Paper: Channel Model for Visible Light Communications using Off-the-shelf Scooter Taillight,” in Proc. IEEE Vehicular Networking Conference, pp. 170-173, Boston, United States, December 2013.
16
Challenge 1
Notes: Think about illumination

## Slide 17: Simultaneous Transmissions
Lights occupy disjoint sets of pixels (except when very far away: > 1km)
Simultaneous transmissions with no collision, interference, and access delay
Challenge 1

## Slide 18: Talking Pixels
Computer vision: associate pixels with information (distance) and context
V2LC: direct association -Information directly comes from the pixels!
Photogrammetry: sub-meter accuracy for positioning
Challenge 2
www.ionroad.com
Notes: Vision-base method inaccuracy  pixels transmitting information combined with the context in the image
How to estimate relative position? Object recognition + assumption

## Slide 19: Low-Cost Transmitter: Pervasive Existence of Automotive LED lights
Low Cost: LED lights already used extensively for vehicles
Extremely simple driver circuit: USD$2 microcontroller
Aftermarket product is feasible: driver module and/or light module
Challenge 3

## Slide 20: Low-Cost Receiver: Cameras Everywhere
Low cost: cameras already exist in many cars
Aftermarket product is feasible:
  App download for mobile devices
  WiFi/Bluetooth link to light module
Challenge 3
Luxgen’s Eagle View+
360 degree vision coverage

## Slide 21: Conclusion
IoV creates new opportunities for both new applications and huge performance improvements
New challenges need to be addressed:
  Vehicle density and speed
  Association of information and identity
  Market penetration
V2LC: new solution for vehicular communications
  Reliable “point-to-point” V2V communications
  Direct association of information and pixels
  Low-cost system design with aftermarket product options