## Slide 1: Intelligent Transportation System (ITS) User Experiences Group
Progress Report
08.22

## Slide 2
Road
(Focus)
Dashboard
Rearview Mirror
Rearview Mirror
Users view in scooter driving

## Slide 3
It’s dangerous to ride without looking at rearview mirrors

## Slide 4
1 second before the accident

## Slide 5
Unfortunately, the passive rearview mirrors
cannot push proactive warnings toward drivers attention

## Slide 6
Using Tertiary, Proactive Display?

## Slide 7
A Tertiary, Proactive Display may cause more distractions!

## Slide 8
Displaying on the Rearview Mirror Directly
Embedding LCD in the Rearview Mirror
Electronic Rearview Mirror (e.g. Smartphone)

## Slide 9
Displaying on the Rearview Mirror Directly
Embedding LCD in the Rearview Mirror
Electronic Rearview Mirror (e.g. Smartphone)
More direct notification, but only simple warnings

## Slide 10
Rich information that replaces the original rearview can be dangerous
infoVis should be carefully designed
(users can only serially process information by their focus vision)

## Slide 11
Our method: Borrow the concept from Augmented Reality

## Slide 12
Our method: Borrow the concept from Augmented Reality
Augment the real rearview

## Slide 13
Our method: Borrow the concept from Augmented Reality
Visualize the offscreen events

## Slide 14
Touch to Activate the Interactive Mode
When speed = 0

## Slide 15
Auto Deactivate the Interactive Mode
When speed > 0

## Slide 16: Guidelines for designing infoVis in Attention-Limited Conditions
Using pre-attentive features
  Shapes and Colors (Color > Shape) have greate salience to human information processors due to the sharp contrast that they are able to create.
Grouping eases searching
  Finding clusters of visually similar items is easier than locating a single item.
Minimalism
  Lower density displays can result in performance that is as good or better than high density displays in dual-tasking.
Make sure the cues are semantically understandable
  Easily understandable visual cues can be comprehended by peripheral vision without hindering primary task performance.

## Slide 17: Resulting Challenges
How to overlay information accurately on the camera view

## Slide 18: Step 1: User Study with the Simulator
Projector screen to show the virtual environment from the driver’s view
Smartphone screen displays rear view (in virtual environment) + additional markers
Scooter game controller + simple scooter mobility model give the user the ability to react to traffic events.

## Slide 19: Step 1: User Study with the Simulator
SUMO traffic simulator
Report the status of the user controlled vehicle
Report the status of all other non-user controlled vehicles (for rendering in virtual environment)
Then, script an accident scene in the traffic simulator!

## Slide 20: Step 2: User Study in the Real-World
How to overlay information accurately on the camera view
Too Hard!!
Have to cheat…

## Slide 21: Since the main goal is to evaluate the UI…
1. Pick an open road with almost no vehicles.
2. Use road-side LIDAR and cameras to obtain addition location information of neighboring vehicles
3. Use a few controlled vehicles to create potentially hazardous and repeatable scenario.
4. On-board smartphone obtain LIDAR and camera information to calculate necessary markers to be shown in AR.

## Slide 22: Possible Generalization Augmenting Rearview mirror in the car